## Slide 1: Filter Design Techniques Chapter-7
Content and Figures are from Discrete-Time Signal Processing, 2e by Oppenheim, Shafer, and Buck, ©1999-2000 Prentice Hall Inc.

## Slide 2: Filter Design Techniques
Any discrete-time system that modifies certain frequencies
Frequency-selective filters pass only certain frequencies
Filter Design Steps
  Specification
    Problem or application specific
  Approximation of specification with a discrete-time system
    Our focus is to go from spec to discrete-time system
  Implementation
    Realization of discrete-time systems depends on target technology
We already studied the use of discrete-time systems to implement a continuous-time system
  If our specifications are given in continuous time we can use
D/C
xc(t)
yr(t)
C/D
H(ej)

## Slide 3: Filter Specifications
Specifications
  Passband
  Stopband
Parameters
Specs in dB
  Ideal passband gain =20log(1) = 0 dB
  Max passband gain = 20log(1.01) = 0.086dB
  Max stopband gain = 20log(0.001) = -60 dB

## Slide 4: Butterworth Lowpass Filters
Passband is designed to be maximally flat
The magnitude-squared function is of the form

## Slide 5: Filter Design by Impulse Invariance
Remember impulse invariance
  Mapping a continuous-time impulse response to discrete-time
  Mapping a continuous-time frequency response to discrete-time
If the continuous-time filter is bandlimited to
If we start from discrete-time specifications
- Start with discrete-time spec in terms of 
  Go to continuous-time =  /T and design continuous-time filter
  Use impulse invariance to map it back to discrete-time = T
Works best for bandlimited filters due to possible aliasing

## Slide 6: Impulse Invariance of System Functions
Develop impulse invariance relation between system functions
Partial fraction expansion of transfer function
Corresponding impulse response
Impulse response of discrete-time filter
System function
Pole s=sk in s-domain transform into pole at

## Slide 7: Impulse Invariance of System Functions
Develop impulse invariance relation between system functions
Partial fraction expansion of transfer function
Corresponding impulse response
Impulse response of discrete-time filter
System function
Pole s=sk in s-domain transform into pole at
Why?

## Slide 8: Example
Impulse invariance applied to Butterworth
Since sampling rate Td cancels out we can assume Td=1
Map spec to continuous time
Butterworth filter is monotonic so spec will be satisfied if
Determine N and c to satisfy these conditions

## Slide 9: Example Cont’d
Satisfy both constrains
Solve these equations to get
Put and N in
N must be an integer so we round it up to meet the spec
Poles of transfer function
The transfer function
Mapping to z-domain

## Slide 10: Example Cont’d
Satisfy both constrains
Solve these equations to get
Put and N in
N must be an integer so we round it up to meet the spec
Poles of transfer function
The transfer function
Mapping to z-domain

## Slide 11: Filter Design by Bilinear Transformation
Get around the aliasing problem of impulse invariance
Map the entire s-plane onto the unit-circle in the z-plane
  Nonlinear transformation
  Frequency response subject to warping
Bilinear transformation
Transformed system function
We can solve the transformation for z as
Maps the left-half s-plane into the inside of the unit-circle in z
  Stable in one domain would stay in the other depending on value of

## Slide 12: Bilinear Transformation
On the unit circle put the transform becomes
To derive the relation between  and 
Which yields

## Slide 13: Bilinear Transformation

## Slide 14: Bilinear Transformation

## Slide 15: Example
Bilinear transform applied to Butterworth
Apply bilinear transformation to specifications
We can assume Td=1 and apply the specifications to
To get

## Slide 16: Example Cont’d
Solve N and c
The resulting transfer function has the following poles
Resulting in
Applying the bilinear transform yields