## Slide 2: Chapter No 6 : BJTs
Introduction

## Slide 3: Chapter 6 CLOs
1. The physical structure of the bipolar transistor and how it works.
2. How the voltage between two terminals of the transistor controls the current that flows through the third terminal, and the equations that describe these current–voltage characteristics.
3. How to analyze and design circuits that contain bipolar transistors, resistors, and dc sources.
4. How the transistor can be used to make an amplifier.
5. How to obtain linear amplification from the fundamentally nonlinear BJT.
6. The three basic ways for connecting a BJT to be able to construct amplifiers with different properties.
7. Practical circuits for bipolar-transistor amplifiers that can be constructed by using discrete components.

## Slide 4: Mapping topics to sections
SNO | Topic | Section
1 | Device Structure & Physical Operation Current-Voltage Characteristics | 6.1,6.2
2 | BJT Circuit at DC | 6.3
3 | Applying the BJT in Amplifier Design | 6.4
4 | Small-Signal Operations and Models | 6.5
5 | Basic BJT Amplifier Configurations | 6.6
6 | Biasing in BJT Amplifier Circuit | 6.7
7 | Discrete-Circuit BJT Amplifier Transistor Breakdown and Temperature Effect | 6.8, 6.9

## Slide 5: Class Lecture Sequence

## Slide 6
  Basic Purpose
  [1] To electronically switch (no moving parts) a signal on or off (high/low)
  [2] To amplify signals
  [3] Oscillators
  Role in Modern Electronics
    Basic building blocks for all modern electronics
    Microprocessors, Microcontrollers, Computers, Digital watches, Digital Logic Circuits, Cell Phones….
Microprocessor
PC & Cell Phones
Motor Controllers
Headphones
Notes: ROADMAP OF BUILD TRANSISTOR -> PROPERTIES

## Slide 7
Early 20th century, vacuum tube were used as signal amplifiers & switches.
Use of vacuum tube* resulted in extremely large, fragile, energy inefficient, and expensive electronics.
Evolution of electronics required device that was small, light weight, robust, reliable, cheap to manufacture, energy efficient…
Reason for Transistor’s Invention:
Vacuum Tube Radios
ENIAC : 17, 468 vacuum tubes

## Slide 8: Tubes used in old electronics equipment

## Slide 9: Tubes Amplifiers

## Slide 10: The Transistor is Born
Bell Labs (1947): Bardeen, Brattain, and Shockley
Originally made of germanium
Current transistors made of doped silicon

## Slide 11: Introduction BJTs
Two terminal devices (Resistor,Capacitors, Inductors , diodes)
Transistor is a three terminal device
The basic principle involved is the use of the voltage between two terminals to control the current flowing in the third terminal
Transistors are Asymmetric devices

## Slide 12
Two types of transistors (NPN, & PNP)
Four modes of operation
At least three type of configuration
Many applications; but we will concentrate on two, that is amplifier and switch
Many types of biasing arrangements but we will discuss only four
Low frequency and high frequency responses

## Slide 13
A voltage dependent current source
Key element for my Amplifier
Amplifier

## Slide 14: Analogies

## Slide 15
Transistor is nothing but a variable resistor. The resistance value of Transistor is changed by the Base current (BJT) or Gate voltage (FET). The value of resistance varies between Zero and Infinity. When the resistance is Zero the transistor operates in Saturation mode. For specific Base current, if the resistance reached Zero after that increasing the Base current will not have any effect on the collector current. The same way when the Base current is Zero the Transistor resistance is Infinity.
Analogy-1

## Slide 16
Output current can toggle between large and small
(Switching  Digital logic; create 0s and 1s)
Small change in ‘valve’ (3rd terminal) creates Large
change in output between 1st and 2nd terminal
(Amplification  Analog applications; Turn 0.5  50)
Terminal -3
Terminal -2
Terminal -1
Analogy-2

## Slide 17: PNP transistor amplifier action
IN (small)
OUT (large)
Clearly this works in common emitter
configuration
Analogy-2

## Slide 18
Analogy-3

## Slide 19: Analogy-4
Collector
Base
Emitter

## Slide 20: Review of some concepts

## Slide 21: Carrier injection

## Slide 22: Asymmetric Doping

## Slide 23
NPN Transistor Simplified Structure
Three regions & two junctions

## Slide 24
PNP Transistor Simplified Structure

## Slide 25
NPN Transistor Modes of Operations
As per our text book
For Amplifier

## Slide 26: BJT Modes of Operation
Find out why not useful

## Slide 27: BJT Modes of Operation

## Slide 28: Symbol and basing of NPN and PNP transistors
Lowest
Low
High
Lowest
Low
High

## Slide 30: Can we model transistor as two back to back connected diodes?
From above figure it can be implied that D1 carries a current and D2 does not. Meaning we should anticipate current flow from the base to emitter but no current through the collector .
If this was true then transistor would not operate as voltage controlled current source and would prove of little value

## Slide 31: Then what is different here ?
Emitter is heavily doped
Base is lightly doped
Base is very thin
Area of collector is much greater then emitter
Summary: In active mode an npn bipolar transistor carriers a large number of electrons from the emitter, through the base , to the collector while drawing a small current of holes through the base terminal

## Slide 33
BJT Cross Sectional View
Note that the collector is very large and virtually surrounds the base- emitter region thus no electrons escapes from being collected here.
This makes α very close to unity
The device is not symmetrical so emitter and collector cannot be interchanged.
A more realistic cross section of an npn BJT

## Slide 34: Question
It is highly desirable to have the electrons from emitter to base at a much higher level than the holes from base to emitter. Which is accomplished by fabricating the device with a heavily doped emitter and a lightly doped base; that is, the device is designed to have a high density of electrons in the emitter and a low density of holes in the base.
WHY ?

## Slide 35: Important questions
How do electrons travel through the base?
  Diffusion
  Drift
How does resulting current depends upon terminal voltages?
How large is the base current?

## Slide 36: NPN Transistor Function
The Emitter Region is highly doped n-type material, so high density of electrons
  Thus a large quantity of electrons flow from emitter to base
The base is lightly doped and it’s width is smaller than the emitter and collector, so low density of holes
  Thus the quantity of holes flowing from base to emitter is very small compared to the electrons flowing in from the emitter

## Slide 37
Because base is very thin and lightly doped, the electric field is negligible ,meaning negligible drift current and majority of current is by diffusion mechanism

## Slide 38: Further elaboration on current flow in transistor

## Slide 39
The minority carrier distribution in the base results from the boundary conditions imposed by the two junctions.
It is not an exponentially decaying distribution, which would result if the base region were infinitely thick.
Furthermore, the reverse bias on the collector–base junction causes the electron concentration at the collector side of the base to be zero.
Further elaboration on current flow in transistor

## Slide 40
NPN Transistor Current Flows
The recombination of electrons and holes in base region makes the electrons concentration deviate from the straight line profile
Once the diffusing electrons reach the Base-Collector depletion region boundary, they will be swept away due to collector being more positive than base

## Slide 41
+
+
+
+
+
+
+
+
+
-
+
-
+
-
+
-
B
C
E
E