## Slide 1: BJT-Lecture

## Slide 2: Dr. Usman covered chapter 6 until 6.5.1: the collector current and its transconductance
6.1 Device Structure and Physical Operation
  6.1.1 Simplified Structure and Modes of Operation
  6.1.2 Operation of the npn Transistor in the Active Mode
  6.1.3 Structure of Actual Transistors
  6.1.4 Operation in the Saturation Mode
6.2 Current–Voltage Characteristics
  6.2.1 Circuit Symbols and Conventions
  6.2.3 Dependence of iC on the Collector Voltage—The Early Effect
6.3 BJT Circuits at DC
6.4 Applying the BJT in Amplifier Design
  6.4.2 The Voltage Transfer Characteristic (VTC)
  6.4.4 The Small-Signal Voltage Gain
6.5 Small-Signal Operation and Models
  6.5.1 The Collector Current and the Transconductance

## Slide 3: Some of the graphs to be kept in mind

## Slide 4
Graphical Analysis: Locating Bias Point
Point Y : vBE = 0.5
Point Z : BJT leave the active mode
Determine Load Line
Which point on Load line
Set of Graphs
Note that we have set of graphs corresponding to each

## Slide 6
Note :As we increase IB The Q point moves upward, that is closer to saturation region

## Slide 7
With increasing R the slope decreases

## Slide 8
What is observation Here?

## Slide 9
6.4 Applying the BJT in Amplifier Design
  6.4.2 The Voltage Transfer Characteristic (VTC)
  6.4.4 The Small-Signal Voltage Gain

## Slide 10: BJT as Amplifier

## Slide 11: BJT as Amplifier
when operated in the active mode, the BJT functions as a voltage-controlled current source: the base–emitter voltage controls the collector current
Although the control relationship is nonlinear (exponential), we will shortly devise a method for obtaining almost-linear amplification from this fundamentally nonlinear device.

## Slide 12
A voltage-controlled current source can serve as a transconductance amplifier, that is, an amplifier whose input signal is a voltage and whose output signal is a current
A simple way to convert a transconductance amplifier to a voltage amplifier is to pass the output current through a resistor and take the voltage across the resistor as the output.
BJT as Amplifier

## Slide 13: The Voltage Transfer Characteristic (VTC)
A very useful tool that yields great insight into the operation of an amplifier circuit is its voltage transfer characteristic (VTC). This is simply a plot of the output voltage versus the input voltage.( Graph)

## Slide 14
vO

## Slide 15
Note that the output voltage is taken between the collector and ground, rather than simply across Rc. This is done because of the need to maintain a ground reference throughout the circuit. The output voltage is given by
The out put is 180 Deg. Phase shifted
(x-y) For Cutoff mode and
(y-Z) Active mode
Saturation mode
For greater than that at point Z,
the transistor operates in the saturation region and decreases very slowly

## Slide 16
The VTC indicates that the segment of greatest slope (and hence potentially the largest amplifier gain) is that labeled YZ, which corresponds to operation in the active mode. An expression for the segment YZ can be obtained by
This is obviously a nonlinear relationship.
linear (or almost-linear) amplification can be obtained by using the technique of biasing the BJT.

## Slide 17: Biasing the BJT to Obtain Linear Amplification
Biasing enables us to obtain almost-linear amplification from the BJT.
A dc voltage is selected to obtain operation at a point Q on the segment YZ of the VTC.
observe that the coordinates of Q are the dc voltages and which are related by

## Slide 18
Biasing BJT for Linear Amplification

## Slide 19
Biasing BJT for Linear Amplification

## Slide 20
Biasing BJT for Linear Amplification

## Slide 21
Next the signal to be amplified a function of time t is superimposed on the bias voltage . Thus the total instantaneous value of becomes

## Slide 22
The Small-Signal Voltage Gain

## Slide 23
The Small-Signal Voltage Gain

## Slide 24
We make the following observations on this expression for the voltage gain:
The gain is negative, which signifies that the amplifier is inverting; that is, there is a 180 phase shift between the input and the output
2. The gain is proportional to the collector bias current and to the load resistance

## Slide 25
The simple expression shows that to maximize the voltage gain we should use as large a voltage drop across RC as possible.
For a given value of VCC, Eq. (6.32) indicates that to increase VRC we have to operate at a lower VCE. However, a lower VCE means a bias point Q close to the end of the active-region segment, which might not leave sufficient room for the negative-output signal swing without the amplifier entering the saturation region. If this happens, the negative peaks of the waveform of vce will be flattened.
Placing Q too high on this segment not only results in reduced gain (because VRC is lower) but could possibly limit the available range of positive signal swing. At the positive end, the limitation is imposed by the BJT cutting off, in which event the positive-output peaks would be clipped off at a level equal to VCC.

## Slide 26: Example 6.13
Consider an amplifier circuit using a BJT having IS = A, a collector resistance RC = 6.8 kΩ, and a power supply VCC = 10 V.
Determine the value of the bias voltage VBE required to operate the transistor
at VCE = 3.2 V. What is the corresponding value of IC?
(b) Find the voltage gain Av at this bias point. If an input sine-wave signal of 5-mV peak amplitude is superimposed on VBE, find the amplitude of the output sine-wave signal (assume linear operation).
(c) Find the positive increment in vBE (above VBE) that drives the transistor to the edge of saturation, where vCE = 0.3 V.
(d) Find the negative increment in vBE that drives the transistor to within 1% of cutoff (i.e., to vCE = 0.99VCC).

## Slide 27
Determine the value of the bias voltage VBE required to operate the transistor
at VCE = 3.2 V. What is the corresponding value of IC?

## Slide 28
Voltage gain X input Voltage= Output voltage
(b) Find the voltage gain Av at this bias point. If an input sine-wave signal of 5-mV peak amplitude is superimposed on VBE, find the amplitude of the output sine-wave signal (assume linear operation).
(c) Find the positive increment in vBE (above VBE) that drives the transistor to the edge of saturation, where vCE = 0.3 V.

## Slide 29
(d) Find the negative increment in vBE that drives the transistor to within 1% of cutoff (i.e., to vCE = 0.99VCC).

## Slide 30
Assignment # 4
Example :6.14 and
Problems: 6.28, 6.29, 6.39

## Slide 31: Small-Signal Operation and Models

## Slide 32
Small Signal Operation and Models

## Slide 33
Transconductance

## Slide 34
Transconductance
DC
SS
gm is the
“transconductance”

## Slide 35
Transconductance
gm varies with variation of Q point
The signal amplitude should be small enough that operation is restricted to an almost linear segment of the
iC-vBE exponential curve

## Slide 36
Base Current and Input Resistance

## Slide 37
Emitter Current and Input Resistance

## Slide 38
Also Do Exercise 6.36 and 6.37 as part of assignment

## Slide 39
Voltage Gain

## Slide 40
Separating the DC & Signal Quantities
The total DC and Small signal circuit is shown.
The DC analysis yield the currents and voltages based on the relevant equations.
The DC sources do no change their values when the signal is applied.
We can replace DC voltages by short circuits and current sources by open circuits respectively to get the Small Signal Model.

## Slide 41
Separating the DC & Signal Quantities
The Small signal circuit is shown.
This circuit is useful only to analyze signal voltages and currents.
This is not an actual amplifier circuit.
This circuit shows all the incremental currents and voltages that occur due to applied small signal at the base.

## Slide 42: The Hybrid –π Model of BJT
Ie in terms of base resistance
Ie in terms of emitter resistance

## Slide 43
The T-Model of BJT

## Slide 44: Small-Signal Models Accounting for the Early Effect
The gain will be reduced, depending upon ro

## Slide 45
Example 6.14
Analyze the transistor amplifier shown in the Figure to determine its voltage gain vo/vi.
Assume β = 100.
Solution:
1. Determine the operating point. For this purpose.
assume vi = 0 and obtain the dc circuit.
The dc currents and voltage will be:
Since VB = 0.7 V is less than VC , the transistor is operating in the active mode

## Slide 46
2. Determine the small-signal model parameters:
3. Replace VBB and VCC with short circuits.
4. Replace the transistor in the circuit by hybrid-π, equivalent-circuit model
5. Analyze of the equivalent circuit

## Slide 47
5. Analyze of the equivalent circuit

## Slide 48: Steps for the Small-Signal Equivalent Circuits
Eliminate the signal source and determine the dc operating point of the BJT and in particular the dc collector current IC.
2. Calculate the values of the small-signal model parameters
3. Eliminate the dc sources by replacing each dc voltage source with a short circuit and each dc current source with an open circuit.
4. Replace the BJT with one of its small-signal equivalent circuit models.
5. Analyze the resulting circuit to determine the required quantities (e.g., voltage gain, input resistance.

## Slide 49
For DC analysis the signal source is removed

## Slide 51: Three Basic Configurations of BJT Amplifier

## Slide 52
Three Basic Configurations

## Slide 53: General Characteristics of each configuration
Power Amplifier as both current and voltage is amplified
Input from base and Output from collector ;
Output is 180 degree out of phase with respect to input
1. Common-Emitter Amplifier - CE

## Slide 54
Only gives amplified current, voltage is unchanged
Input from base output from emitter
Output is in- phase with respect to input

## Slide 55
Input from Emitter and Output from collector ;
Output is in- phase with respect to input

## Slide 56: CE-Amplifier

## Slide 57: CB-Amplifier
Note we preferred T-model as there was an external-resistor in the emitter

## Slide 58
What source sees
What Load sees

## Slide 59: Simple cc circuit

## Slide 61: Summary of BJT Configurations

## Slide 62: Lecture No 13
Input/output Impedances
&
Transistor Configuration

## Slide 63: General Characteristics of an Amplifier
Gain
Input /output impedance
Frequency response
Bandwidth
Efficiency
Immunity to Noise/ Temperature variation
Immunity to differences due to manufacture processes
Cost, rigidness , reliability (MTBF)

## Slide 65
The transistor shown in the Figure is biased with a constant current source I = 1 mA and has β = 100 and VA = 100 V.
(a) Find the dc voltages at the base, emitter, and collector.
(b) Find gm, rπ , and ro.
Example
Solution
(a)
(b)

## Slide 66: Cascaded Amplifier
Why did we use different stages of amplifier?
Example from Chapter No 1
High i/p impedance
Low o/p impedance

## Slide 67
Another Example to show effect of Impedances
Voltage Buffer

## Slide 69
Amplifier Characteristics
May affected by RL

## Slide 70
Amplifier Characteristics
For measuring Ro
Signal source is replaced with short circuit
Test voltage vx is applied
The resultant current ix is measured

## Slide 71
Amplifier Characteristics

## Slide 72
Amplifier Characteristics
Triangle in blue = rectangle in blue below
Can you identify and differentiate various gains here
Note the difference between