## Slide 1
Instructor: Dr. Arbab Latif
EE-222: Microprocessor Systems
Nested Loops
and
Stack & Call

## Slide 2: Loop
for (init; condition; calculation)
{
do something
}
END
calculation
Do something
Condition
No
Yes
init

## Slide 3: Loop
Write a program that executes the instruction “ADD R30,R31” 9 times.
Solution:
.ORG 00
LDI R16,9 ;R16 = 9
L1: ADD R30,R31
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 4: Loop
Write a program that calculates the result of 9+8+7+…+1
Solution:
.ORG 00
LDI R16, 9 ;R16 = 9
LDI R17, 0 ;R17 = 0
L1: ADD R17,R16 ;R17 = R17 + R16
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 5: Loop
Write a program that calculates the result of 20+19+18+17+…+1
Solution:
.ORG 00
LDI R16, 20 ;R16 = 20
LDI R17, 0 ;R17 = 0
L1: ADD R17,R16 ;R17 = R17 + R16
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 6: Stack
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
000A
000B
000C
000D
ORG 0
LDI R16,HIGH(RAMEND)
OUT SPH,R16
LDI R16,LOW(RAMEND)
OUT SPL,R16
LDI R20,0x10
LDI R21, 0x20
LDI R22,0x30
PUSH R20
PUSH R21
PUSH R22
POP R21
POP R0
POP R20
L1: RJMP L1
Address
Code
SP
Memory
R20:
R21:
$00
$10
$00
$20
$00
$00
$30
R22:
R0:
$10
$20
$30
0000

## Slide 7: Calling a Function
0000
0001
0002
0003
0004
0005
0006
0008
0009
000A
000A
000B
000C
000D
LDI R16,HIGH(RAMEND)
OUT SPH,R16
LDI R16,LOW(RAMEND)
OUT SPL,R16
LDI R20,15
LDI R21,5
CALL FUNC_NAME
INC R20
L1: RJMP L1
FUNC_NAME:
ADD R20,R21
SUBI R20,3
RET
Code
Address
0006
opCode
operand
940E 000A
Machine code:
SP
Stack
PC:
0004
0005
0006
0008
000A
000B
000C
08
00
0008
0009
To execute a call:
  Address of the next instruction is saved
  PC is loaded with the appropriate value