## Slide 1: Assembly
EE222 – Microprocessor Systems
Arbab Latif
Spring 2021
Resources:
Assembly Language for Intel based computers by Kip R. Irvine (Section 2.1.2)

## Slide 2: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 3: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 4: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output

## Slide 5: Multi-Stage Pipeline
Pipelining makes it possible for processor to execute instructions in parallel
Instruction execution divided into discrete stages
Example of a non-pipelined processor. Many wasted cycles.

## Slide 6: Pipelined Execution
More efficient use of cycles, greater throughput of instructions:
For k states and n instructions, the number of required cycles is:
k + (n – 1)

## Slide 7: Wasted Cycles (pipelined)
When one of the stages requires two or more clock cycles, clock cycles are again wasted.
For k states and n instructions, the number of required cycles is:
k + (2n – 1)

## Slide 8: Superscalar
A superscalar processor has multiple execution pipelines. In the following, note that Stage S4 has left and right pipelines (u and v).
For k states and n instructions, the number of required cycles is:
k + n

## Slide 9: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  address placed on address bus
  Read Line (RD) set low
  CPU waits one cycle for memory to respond
  Read Line (RD) goes to 1, indicating that the data is on the data bus

## Slide 10: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 11: How a Program Runs

## Slide 12: Multitasking
OS can run multiple programs at the same time.
Multiple threads of execution within the same program.
Scheduler utility assigns a given amount of CPU time to each running program.
Rapid switching of tasks
  gives illusion that all programs are running at once
  the processor must support task switching.

## Slide 13: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 14: Modes of Operation
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 15: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 16: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 17: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.

## Slide 18: Accessing Parts of Registers
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 19: Index and Base Registers
Some registers have only a 16-bit name for their lower half:

## Slide 20: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 21: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 22: Status Flags
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4
Parity
  sum of 1 bits is an even number

## Slide 23: Floating-Point, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations

## Slide 24: Segmented Memory
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment

## Slide 25: Calculating Linear Addresses
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0

## Slide 26: Multi-Segment Model
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program

## Slide 27: Paging
Supported directly by the CPU
Divides each segment into 4096-byte blocks called pages
Sum of all programs can be larger than physical memory
Part of running program is in memory, part is on disk
Virtual memory manager (VMM) – OS utility that manages the loading and unloading of pages
Page fault – issued by CPU when a page must be loaded from disk

## Slide 28: Intel D850MD Motherboard
dynamic RAM
Intel 486 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audo chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 29: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 30: Levels of Input-Output
Level 3: Call a library function (C++, Java)
  easy to do; abstracted from hardware; details hidden
  slowest performance
Level 2: Call an operating system function
  specific to one OS; device-independent
  medium performance
Level 1: Call a BIOS (basic input-output system) function
  may produce different results on different systems
  knowledge of hardware required
  usually good performance

## Slide 31: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 32: Operand Types
Three basic types of operands:
  Immediate – a constant integer (8, 16, or 32 bits)
    value is encoded within the instruction
  Register – the name of a register
    register name is converted to a number and encoded within the instruction
  Memory – reference to a location in memory
    memory address is encoded within the instruction, or a register holds the address of a memory location

## Slide 33: Instruction Operand Notation

## Slide 34: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format

## Slide 35: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination. Syntax:
    MOV destination,source
No more than one memory operand permitted
CS, EIP, and IP cannot be the destination
No immediate to segment moves

## Slide 36: Your turn . . .
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov esi,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
Explain why each of the following MOV statements are invalid:
immediate move to DS not permitted
size mismatch
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted

## Slide 37: Zero Extension
mov bl,10001111b
movzx ax,bl ; zero-extension
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.
The destination must be a register.

## Slide 38: Sign Extension
mov bl,10001111b
movsx ax,bl ; sign extension
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit.
The destination must be a register.

## Slide 39: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 40: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB+1 ; AL = 20h
mov al,[arrayB+1] ; alternative notation
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
Q: Why doesn't arrayB+1 produce 11h?

## Slide 41: Direct-Offset Operands (cont)
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax,[arrayW+2]
; AX = 2000h
mov ax,[arrayW+4]
; AX = 3000h
mov eax,[arrayD+4]
; EAX = 00000002h
A constant offset is added to a data label to get an effective address (EA). The address is dereferenced to get the value inside its memory location.
; Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??
What will happen when they run?

## Slide 42: Your turn. . .
Write a program that rearranges the values of three doubleword values in the following array as: 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the third array value and copy the value in EAX to the first array position.
Step1: copy the first value into EAX and exchange it with the value in the second position.
mov eax,arrayD
xchg eax,[arrayD+4]
xchg eax,[arrayD+8]
mov arrayD,eax

## Slide 43: Evaluate this . . .
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
mov ax,myBytes
add ax,[myBytes+1]
add ax,[myBytes+2]
Any other possibilities?

## Slide 44: Evaluate this . . . (cont)
.data
myBytes BYTE 80h,66h,0A5h
How about the following code. Is anything missing?
movzx ax,myBytes
mov bl,[myBytes+1]
add ax,bx
mov bl,[myBytes+2]
add ax,bx ; AX = sum
Yes: Move zero to BX before the MOVZX instruction.

## Slide 45: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 46: INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
INC destination
    Logic: destination  destination + 1
DEC destination
    Logic: destination  destination – 1

## Slide 47: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 48: Your turn...
Show the value of the destination operand after each of the following instructions executes:
.data
myByte BYTE 0FFh, 0
.code
mov al,myByte ; AL =
mov ah,[myByte+1] ; AH =
dec ah ; AH =
inc al ; AL =
dec ax ; AX =
FFh
00h
FFh
00h
FEFFh

## Slide 49: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction

## Slide 50: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code
mov eax,var1
add eax,var2
add ax,0FFFFh
add eax,1
sub ax,1
; 00010000h
; 00030000h
; 0003FFFFh
; 00040000h
; 0004FFFFh
; EAX

## Slide 51: NEG (negate) Instruction
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Reverses the sign of an operand. Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?

## Slide 52: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1, OF = 0
neg [valB + 1] ; CF = 0, OF = 0
neg valC ; CF = 1, OF = 1
The processor implements NEG using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 53: Implementing Arithmetic Expressions
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36
HLL compilers translate mathematical expressions into assembly language. You can do it also. For example:
Rval = -Xval + (Yval – Zval)

## Slide 54: Your turn...
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language. Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.

## Slide 55: Flags Affected by Arithmetic
The ALU has a number of status flags that reflect the outcome of arithmetic (and bitwise) operations
  based on the contents of the destination operand
Essential flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range
  Overflow flag – set when signed value is out of range
The MOV instruction never affects the flags.

## Slide 56: Zero Flag (ZF)
mov cx,1
sub cx,1 ; CX = 0, ZF = 1
mov ax,0FFFFh
inc ax ; AX = 0, ZF = 1
inc ax ; AX = 1, ZF = 0
The Zero flag is set when the result of an operation produces zero in the destination operand.
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.

## Slide 57: Sign Flag (SF)
mov cx,0
sub cx,1 ; CX = -1, SF = 1
add cx,2 ; CX = 1, SF = 0
The Sign flag is set when the destination operand is negative. The flag is clear when the destination is positive.
The sign flag is a copy of the destination's highest bit:
mov al,0
sub al,1 ; AL = 11111111b, SF = 1
add al,2 ; AL = 00000001b, SF = 0

## Slide 58: Signed and Unsigned Integers A Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the programmer, are solely responsible for using the correct data type with each instruction
Added Slide. Gerald Cahill, Antelope Valley College

## Slide 59: Overflow and Carry Flags A Hardware Viewpoint
How the ADD instruction modifies OF and CF:
  OF = (carry out of the MSB) XOR (carry into the MSB)
  CF = (carry out of the MSB)
How the SUB instruction modifies OF and CF:
  NEG the source and ADD it to the destination
  OF = (carry out of the MSB) XOR (carry into the MSB)
  CF = INVERT (carry out of the MSB)
MSB = Most Significant Bit (high-order bit)
XOR = eXclusive-OR operation
NEG = Negate (same as SUB 0,operand )

## Slide 60: Carry Flag (CF)
The Carry flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
mov al,0FFh
add al,1 ; CF = 1, AL = 00
; Try to go below zero:
mov al,0
sub al,1 ; CF = 1, AL = FF

## Slide 61: Your turn . . .
mov ax,00FFh
add ax,1 ; AX= SF= ZF= CF=
sub ax,1 ; AX= SF= ZF= CF=
add al,1 ; AL= SF= ZF= CF=
mov bh,6Ch
add bh,95h ; BH= SF= ZF= CF=
mov al,2
sub al,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:
0100h 0 0 0
00FFh 0 0 0
00h 0 1 1
01h 0 0 1
FFh 1 0 1

## Slide 62: Overflow Flag (OF)
The Overflow flag is set when the signed result of an operation is invalid or out of range.
; Example 1
mov al,+127
add al,1 ; OF = 1, AL = ??
; Example 2
mov al,7Fh ; OF = 1, AL = 80h
add al,1
The two examples are identical at the binary level because 7Fh equals +127. To determine the value of the destination operand, it is often easier to calculate in hexadecimal.

## Slide 63: A Rule of Thumb
When adding two integers, remember that the Overflow flag is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF =
mov al,-2
add al,+127 ; OF =
1
0

## Slide 64: Your turn . . .
mov al,-128
neg al ; CF = OF =
mov ax,8000h
add ax,2 ; CF = OF =
mov ax,0
sub ax,2 ; CF = OF =
mov al,-5
sub al,+125 ; OF =
What will be the values of the given flags after each operation?
1 1
0 0
1 0
1

## Slide 65: OFFSET Operator
OFFSET returns the distance in bytes, of a label from the beginning of its enclosing segment
  Protected mode: 32 bits
  Real mode: 16 bits
The Protected-mode programs we write use the flat memory model.

## Slide 66: OFFSET Examples
.data
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.code
mov esi,OFFSET bVal ; ESI = 00404000
mov esi,OFFSET wVal ; ESI = 00404001
mov esi,OFFSET dVal ; ESI = 00404003
mov esi,OFFSET dVal2 ; ESI = 00404007
Let's assume that the data segment begins at 00404000h:

## Slide 67: PTR Operator
.data
myDouble DWORD 12345678h
.code
mov ax,myDouble ; error – why?
mov ax,WORD PTR myDouble ; loads 5678h
mov WORD PTR myDouble,4321h ; saves 4321h
Overrides the default type of a label (variable). Provides the flexibility to access part of a variable.
Recall that little endian order is used when storing data in memory (see Section 3.4.9).

## Slide 68: Little Endian Order
Little endian order refers to the way Intel stores integers in memory.
Multi-byte integers are stored in reverse order, with the least significant byte stored at the lowest address
For example, the doubleword 12345678h would be stored as:
When integers are loaded from memory into registers, the bytes are automatically re-reversed into their correct positions.

## Slide 69: PTR Operator Examples
.data
myDouble DWORD 12345678h
mov al,BYTE PTR myDouble
mov al,BYTE PTR [myDouble+1]
mov al,BYTE PTR [myDouble+2]
mov ax,WORD PTR myDouble
mov ax,WORD PTR [myDouble+2]
; AL = 78h
; AL = 56h
; AL = 34h
; AX = 5678h
; AX = 1234h

## Slide 70: PTR Operator (cont)
.data
myBytes BYTE 12h,34h,56h,78h
.code
mov ax,WORD PTR [myBytes]
; AX = 3412h
mov ax,WORD PTR [myBytes+2]
; AX = 7856h
mov eax,DWORD PTR myBytes
; EAX = 78563412h
PTR can also be used to combine elements of a smaller data type and move them into a larger operand. The CPU will automatically reverse the bytes.

## Slide 71: Your turn . . .
.data
varB BYTE 65h,31h,02h,05h
varW WORD 6543h,1202h
varD DWORD 12345678h
.code
mov ax,WORD PTR [varB+2] ; a.
mov bl,BYTE PTR varD ; b.
mov bl,BYTE PTR [varW+2] ; c.
mov ax,WORD PTR [varD+2] ; d.
mov eax,DWORD PTR varW ; e.
Write down the value of each destination operand:
0502h
78h
02h
1234h
12026543h

## Slide 72: TYPE Operator
The TYPE operator returns the size, in bytes, of a single element of a data declaration.
.data
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.code
mov eax,TYPE var1 ; 1
mov eax,TYPE var2 ; 2
mov eax,TYPE var3 ; 4
mov eax,TYPE var4 ; 8

## Slide 73: LENGTHOF Operator
.data
byte1 BYTE 10,20,30
array1 WORD 30 DUP(?),0,0
array2 WORD 5 DUP(3 DUP(?))
array3 DWORD 1,2,3,4
digitStr BYTE "12345678",0
.code
mov ecx,LENGTHOF array1
The LENGTHOF operator counts the number of elements in a single data declaration.
; 3
;32
; 15
; 4
; 9
; 32
LENGTHOF

## Slide 74: SIZEOF Operator
.data
byte1 BYTE 10,20,30
array1 WORD 30 DUP(?),0,0
array2 WORD 5 DUP(3 DUP(?))
array3 DWORD 1,2,3,4
digitStr BYTE "12345678",0
.code
mov ecx,SIZEOF array1
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.
; 3
;64
; 30
; 16
; 9
; 64
SIZEOF

## Slide 75: Spanning Multiple Lines (1 of 2)
.data
array WORD 10,20,
30,40,
50,60
.code
mov eax,LENGTHOF array ; 6
mov ebx,SIZEOF array ; 12
A data declaration spans multiple lines if each line (except the last) ends with a comma. The LENGTHOF and SIZEOF operators include all lines belonging to the declaration:

## Slide 76: Spanning Multiple Lines (2 of 2)
.data
array WORD 10,20
WORD 30,40
WORD 50,60
.code
mov eax,LENGTHOF array ; 2
mov ebx,SIZEOF array ; 4
In the following example, array identifies only the first WORD declaration. Compare the values returned by LENGTHOF and SIZEOF here to those in the previous slide:

## Slide 77: LABEL Directive
Assigns an alternate label name and type to an existing storage location
LABEL does not allocate any storage of its own
Removes the need for the PTR operator
.data
dwList LABEL DWORD
wordList LABEL WORD
intList BYTE 00h,10h,00h,20h
.code
mov eax,dwList ; 20001000h
mov cx,wordList ; 1000h
mov dl,intList ; 00h

## Slide 78: Indirect Addressing
Indirect Operands
Array Sum Example
Indexed Operands
Pointers

## Slide 79: Indirect Operands (1 of 2)
.data
val1 BYTE 10h,20h,30h
.code
mov esi,OFFSET val1
mov al,[esi] ; dereference ESI (AL = 10h)
inc esi
mov al,[esi] ; AL = 20h
inc esi
mov al,[esi] ; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).

## Slide 80: Indirect Operands (2 of 2)
.data
myCount WORD 0
.code
mov esi,OFFSET myCount
inc [esi] ; error: ambiguous
inc WORD PTR [esi] ; ok
Use PTR to clarify the size attribute of a memory operand.
Should PTR be used here?
add [esi],20
yes, because [esi] could point to a byte, word, or doubleword

## Slide 81: Array Sum Example
.data
arrayW WORD 1000h,2000h,3000h
.code
  mov esi,OFFSET arrayW
  mov ax,[esi]
  add esi,2 ; or: add esi,TYPE arrayW
  add ax,[esi]
  add esi,2
  add ax,[esi] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.
ToDo: Modify this example for an array of doublewords.

## Slide 82: Indexed Operands
.data
arrayW WORD 1000h,2000h,3000h
.code
mov esi,0
mov ax,[arrayW + esi] ; AX = 1000h
mov ax,arrayW[esi] ; alternate format
add esi,2
add ax,[arrayW + esi]
etc.
An indexed operand adds a constant to a register to generate an effective address. There are two notational forms:
[label + reg] label[reg]
ToDo: Modify this example for an array of doublewords.

## Slide 83: Index Scaling*
.data
arrayB BYTE 0,1,2,3,4,5
arrayW WORD 0,1,2,3,4,5
arrayD DWORD 0,1,2,3,4,5
.code
mov esi,4
mov al,arrayB[esi*TYPE arrayB] ; 04
mov bx,arrayW[esi*TYPE arrayW] ; 0004
mov edx,arrayD[esi*TYPE arrayD] ; 00000004
You can scale an indirect or indexed operand to the offset of an array element. This is done by multiplying the index by the array's TYPE:
* Not in the book

## Slide 84: Pointers
.data
arrayW WORD 1000h,2000h,3000h
ptrW DWORD arrayW
.code
mov esi,ptrW
mov ax,[esi] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable.
Alternate format:
ptrW DWORD OFFSET arrayW

## Slide 85: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
LOOP Example
Summing an Integer Array
Copying a String

## Slide 86: JMP Instruction
top:
.
.
jmp top
JMP is an unconditional jump to a label that is usually within the same procedure.
Syntax: JMP target
Logic: EIP  target
Example:
A jump outside the current procedure must be to a special type of label called a global label (see Section 5.5.2.3 for details).

## Slide 87: LOOP Instruction
The LOOP instruction creates a counting loop
Syntax: LOOP target
Logic:
  ECX  ECX – 1
  if ECX != 0, jump to target
Implementation:
  The assembler calculates the distance, in bytes, between the offset of the following instruction and the offset of the target label. It is called the relative offset.
  The relative offset is added to EIP.

## Slide 88: LOOP Example
00000000 66 B8 0000 mov ax,0
00000004 B9 00000005 mov ecx,5
00000009 66 03 C1 L1: add ax,cx
0000000C E2 FB loop L1
0000000E
The following loop calculates the sum of the integers 5 + 4 + 3 +2 + 1:
When LOOP is assembled, the current location = 0000000E (offset of the next instruction). –5 (FBh) is added to the the current location, causing a jump to location 00000009:
00000009  0000000E + FB
offset machine code source code

## Slide 89: Your turn . . .
If the relative offset is encoded in a single signed byte,
(a) what is the largest possible backward jump?
(b) what is the largest possible forward jump?
-128
+127

## Slide 90: Your turn . . .
What will be the final value of AX?
mov ax,6
mov ecx,4
L1:
inc ax
loop L1
How many times will the loop execute?
mov ecx,0
X2:
inc ax
loop X2
10
4,294,967,296

## Slide 91: Nested Loop
If you need to code a loop within a loop, you must save the outer loop counter's ECX value. In the following example, the outer loop executes 100 times, and the inner loop 20 times.
.data
count DWORD ?
.code
mov ecx,100 ; set outer loop count
L1:
mov count,ecx ; save outer loop count
mov ecx,20 ; set inner loop count
L2: .
  .
  loop L2 ; repeat the inner loop
mov ecx,count ; restore outer loop count
loop L1 ; repeat the outer loop

## Slide 92: Summing an Integer Array
.data
intarray WORD 100h,200h,300h,400h
.code
  mov edi,OFFSET intarray ; address of intarray
  mov ecx,LENGTHOF intarray ; loop counter
  mov ax,0 ; zero the accumulator
L1:
  add ax,[edi] ; add an integer
  add edi,TYPE intarray ; point to next integer
loop L1 ; repeat until ECX = 0
The following code calculates the sum of an array of 16-bit integers.

## Slide 93: Your turn . . .
What changes would you make to the program on the previous slide if you were summing a doubleword array?

## Slide 94: Calling a Library Procedure
INCLUDE Irvine32.inc
.code
mov eax,1234h ; input argument
call WriteHex ; show hex number
call Crlf ; end of line
Call a library procedure using the CALL instruction. Some procedures require input arguments. The INCLUDE directive copies in the procedure prototypes (declarations).
The following example displays "1234" on the console:

## Slide 95: Linking to a Library
Your programs link to Irvine32.lib using the linker command inside a batch file named make32.bat.
Notice the two LIB files: Irvine32.lib, and kernel32.lib
  the latter is part of the Microsoft Win32 Software Development Kit (SDK)

## Slide 96: Library Procedures - Overview (1 of 3)
Clrscr - Clears the console and locates the cursor at the upper left corner.
Crlf - Writes an end of line sequence to standard output.
Delay - Pauses the program execution for a specified n millisecond interval.
DumpMem - Writes a block of memory to standard output in hexadecimal.
DumpRegs - Displays the EAX, EBX, ECX, EDX, ESI, EDI, EBP, ESP, EFLAGS, and EIP registers in hexadecimal. Also displays the Carry, Sign, Zero, and Overflow flags.

## Slide 97: Library Procedures - Overview (2 of 3)
Gotoxy - Locates cursor at row and column on the console.
Random32 - Generates a 32-bit pseudorandom integer in the range 0 to FFFFFFFFh.
Randomize - Seeds the random number generator.
RandomRange - Generates a pseudorandom integer within a specified range.
ReadChar - Reads a single character from standard input.
ReadHex - Reads a 32-bit hexadecimal integer from standard input, terminated by the Enter key.
ReadInt - Reads a 32-bit signed decimal integer from standard input, terminated by the Enter key.
ReadString - Reads a string from standard input, terminated by the Enter key.

## Slide 98: Library Procedures - Overview (3 of 3)
SetTextColor - Sets the foreground and background colors of all subsequent text output to the console.
WaitMsg - Displays message, waits for Enter key to be pressed.
WriteBin - Writes an unsigned 32-bit integer to standard output in ASCII binary format.
WriteChar - Writes a single character to standard output.
WriteDec - Writes an unsigned 32-bit integer to standard output in decimal format.
WriteHex - Writes an unsigned 32-bit integer to standard output in hexadecimal format.
WriteInt - Writes a signed 32-bit integer to standard output in decimal format.
WriteString - Writes a null-terminated string to standard output.

## Slide 99: Example 1
.code
call Clrscr
mov eax,500
call Delay
call DumpRegs
Clear the screen, delay the program for 500 milliseconds, and dump the registers and flags.
EAX=00000613 EBX=00000000 ECX=000000FF EDX=00000000
ESI=00000000 EDI=00000100 EBP=0000091E ESP=000000F6
EIP=00401026 EFL=00000286 CF=0 SF=1 ZF=0 OF=0
Sample output:

## Slide 100: Example 2
.data
str1 BYTE "Assembly language is easy!",0
.code
mov edx,OFFSET str1
call WriteString
call Crlf
Display a null-terminated string and move the cursor to the beginning of the next screen line.

## Slide 101: Example 2a
.data
str1 BYTE "Assembly language is easy!",0Dh,0Ah,0
.code
mov edx,OFFSET str1
call WriteString
Display a null-terminated string and move the cursor to the beginning of the next screen line (use embedded CR/LF)

## Slide 102: Example 3
IntVal = 35
.code
mov eax,IntVal
call WriteBin ; display binary
call Crlf
call WriteDec ; display decimal
call Crlf
call WriteHex ; display hexadecimal
call Crlf
Display an unsigned integer in binary, decimal, and hexadecimal, each on a separate line.
0000 0000 0000 0000 0000 0000 0010 0011
35
23
Sample output:

## Slide 103: Example 4
.data
fileName BYTE 80 DUP(0)
.code
mov edx,OFFSET fileName
mov ecx,SIZEOF fileName – 1
call ReadString
Input a string from the user. EDX points to the string and ECX specifies the maximum number of characters the user is permitted to enter.
A null byte is automatically appended to the string.

## Slide 104: Example 5
.code
mov ecx,10 ; loop counter
L1: mov eax,100 ; ceiling value
call RandomRange ; generate random int
call WriteInt ; display signed int
call Crlf ; goto next display line
loop L1 ; repeat loop
Generate and display ten pseudorandom signed integers in the range 0 – 99. Pass each integer to WriteInt in EAX and display it on a separate line.

## Slide 105: Example 6
.data
str1 BYTE "Color output is easy!",0
.code
mov eax,yellow + (blue * 16)
call SetTextColor
mov edx,OFFSET str1
call WriteString
call Crlf
Display a null-terminated string with yellow characters on a blue background.
The background color is multiplied by 16 before being added to the foreground color.

## Slide 106: Stack Operations
Runtime Stack
PUSH Operation
POP Operation
PUSH and POP Instructions
Using PUSH and POP
Example: Reversing a String
Related Instructions

## Slide 107: Runtime Stack
Imagine a stack of plates . . .
  plates are only added to the top
  plates are only removed from the top
  LIFO structure

## Slide 108: Runtime Stack
Managed by the CPU, using two registers
  SS (stack segment)
  ESP (stack pointer) *
* SP in Real-address mode

## Slide 109: PUSH Operation (1 of 2)
A 32-bit push operation decrements the stack pointer by 4 and copies a value into the location pointed to by the stack pointer.

## Slide 110: PUSH Operation (2 of 2)
Same stack after pushing two more integers:
The stack grows downward. The area below ESP is always available (unless the stack has overflowed).

## Slide 111: POP Operation
Copies value at stack[ESP] into a register or variable.
Adds n to ESP, where n is either 2 or 4.
  value of n depends on the attribute of the operand receiving the data

## Slide 112: PUSH and POP Instructions
PUSH syntax:
  PUSH r/m16
  PUSH r/m32
  PUSH imm32
POP syntax:
  POP r/m16
  POP r/m32

## Slide 113: Example: Stack operations
mov eax, 11223344h
mov ebx, 55667788h
mov ecx, 99aabbcch
push eax
push ebx
push ecx
mov esi, esp
mov ecx, 3
mov ebx, 4
call DumpMem
Dump of offset:
----------------------
99aabbcc 55667788 11223344

## Slide 114: Example: Stack operations (cont’d)
mov eax, 11223344h
mov ebx, 55667788h
mov ecx, 99aabbcch
mov edx, 0ddeeff00h
push eax
push ebx
push ecx
push edx
mov esi, esp
mov di, [esi]
mov di, [esi+2]
pop eax
pop bx
pop ax
;di = ff00
;di = ddeeh
;eax = ddeeff00h
;bx = bbcch
;ax = 99aah

## Slide 115: Using PUSH and POP
push esi ; push registers
push ecx
push ebx
mov esi,OFFSET dwordVal ; display some memory
mov ecx,LENGTHOF dwordVal
mov ebx,TYPE dwordVal
call DumpMem
pop ebx ; restore registers
pop ecx
pop esi
Save and restore registers when they contain important values. PUSH and POP instructions occur in the opposite order.

## Slide 116: Example: Nested Loop
mov ecx,100 ; set outer loop count
L1: ; begin the outer loop
push ecx ; save outer loop count
mov ecx,20 ; set inner loop count
L2: ; begin the inner loop
;
;
loop L2 ; repeat the inner loop
pop ecx ; restore outer loop count
loop L1 ; repeat the outer loop
Remember the nested loop we created on page 129? It's easy to push the outer loop counter before entering the inner loop:

## Slide 117: Example: Reversing a String
Use a loop with indexed addressing
Push each character on the stack
Start at the beginning of the string, pop the stack in reverse order, insert each character back into the string
Q: Why must each character be put in EAX before it is pushed?
Because only word (16-bit) or doubleword (32-bit) values can be pushed on the stack.

## Slide 118: Your turn . . .
Write a program so it inputs a list of 32-bit integers from the user, stores the integers in an array and then displays the integers in reverse order.
.data
Arr1 DWORD 5 DUP (0)
str1 BYTE "input an integer", 0
.code
mov edi, OFFSET Arr1
mov ecx, LENGTHOF Arr1
L1: mov edx, offset str1
call WriteString
call crlf
call ReadInt
push eax
mov [edi], eax
add edi, TYPE Arr1
loop L1
mov ecx, LENGTH OF Arr1
L2:
pop eax
call WriteInt
call crlf
loop L2

## Slide 119: Related Instructions
PUSHFD and POPFD
  push and pop the EFLAGS register
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
  PUSHA and POPA do the same for 16-bit registers

## Slide 120: Your Turn . . .
Write a program that does the following:
  Assigns integer values to EAX, EBX, ECX, EDX, ESI, and EDI
  Uses PUSHAD to push the general-purpose registers on the stack
  Using a loop, your program should pop each integer from the stack and display it on the screen

## Slide 121: Example: PUSHAD
.data
varD DWORD 1122h, 3344h, 5566h, 7788h, 99aah, 0bbcch
.code
mov eax, varD ;
mov ebx, varD+4
mov ecx, varD+8
mov edx, varD+12
mov esi, varD+16
mov edi, varD+20
pushad
mov ecx, 8
L1: pop eax
call WriteHex
call crlf
loop L1

## Slide 122: Defining and Using Procedures
Creating Procedures
Documenting Procedures
Example: SumOf Procedure
CALL and RET Instructions
Nested Procedure Calls
Local and Global Labels
Procedure Parameters
Flowchart Symbols
USES Operator

## Slide 123: Creating Procedures
Large problems can be divided into smaller tasks to make them more manageable
A procedure is the ASM equivalent of a Java or C++ function
Following is an assembly language procedure named sample:
sample PROC
  .
  .
  ret
sample ENDP

## Slide 124: Documenting Procedures
A description of all tasks accomplished by the procedure.
Receives: A list of input parameters; state their usage and requirements.
Returns: A description of values returned by the procedure.
Requires: Optional list of requirements called preconditions that must be satisfied before the procedure is called.
Suggested documentation for each procedure:
If a procedure is called without its preconditions having been satisfied, the procedure's creator makes no promise that it will work.

## Slide 125: Example: SumOf Procedure
;---------------------------------------------------------
SumOf PROC
;
; Calculates and returns the sum of three 32-bit integers.
; Receives: EAX, EBX, ECX, the three integers. May be
; signed or unsigned.
; Returns: EAX = sum, and the status flags (Carry,
; Overflow, etc.) are changed.
; Requires: nothing
;---------------------------------------------------------
  add eax,ebx
  add eax,ecx
  ret
SumOf ENDP

## Slide 126: Example: Calling Procedure
. data
intArray DWORD 1, 2, 3
sum DWORD ?
.code
mov eax, intArray
mov ebx, [intArray+4]
mov ecx, [intArray+8]
call SumOf
mov sum, eax
SumOf PROC
; Calculates and returns the
; sum of three 32-bit integers.
  add eax,ebx
  add eax,ecx
  ret
SumOf ENDP

## Slide 127: CALL and RET Instructions
The CALL instruction calls a procedure
  pushes offset of next instruction on the stack
  copies the address of the called procedure into EIP
The RET instruction returns from a procedure
  pops top of stack into EIP

## Slide 128: CALL-RET Example (1 of 2)
main PROC
  00000020 call MySub
  00000025 mov eax,ebx
  .
  .
main ENDP
MySub PROC
  00000040 mov eax,edx
  .
  .
  ret
MySub ENDP
0000025 is the offset of the instruction immediately following the CALL instruction
00000040 is the offset of the first instruction inside MySub

## Slide 129: CALL-RET Example (2 of 2)
The CALL instruction pushes 00000025 onto the stack, and loads 00000040 into EIP
The RET instruction pops 00000025 from the stack into EIP
(stack shown before RET executes)

## Slide 130: Nested Procedure Calls
By the time Sub3 is called, the stack contains all three return addresses:

## Slide 131: Local and Global Labels
main PROC
jmp L2 ; error
L1:: ; global label
exit
main ENDP
sub2 PROC
L2: ; local label
jmp L1 ; ok
ret
sub2 ENDP
A local label is visible only to statements inside the same procedure. A global label is visible everywhere.

## Slide 132: Procedure Parameters (1 of 3)
A good procedure might be usable in many different programs
  but not if it refers to specific variable names
Parameters help to make procedures flexible because parameter values can change at runtime

## Slide 133: Procedure Parameters (2 of 3)
ArraySum PROC
  mov esi,0 ; array index
  mov eax,0 ; set the sum to zero
mov ecx,LENGTHOF myarray ; set number of elements
L1: add eax,myArray[esi] ; add each integer to sum
  add esi,4 ; point to next integer
  loop L1 ; repeat for array size
  mov theSum,eax ; store the sum
ret
ArraySum ENDP
The ArraySum procedure calculates the sum of an array. It makes two references to specific variable names:
What if you wanted to calculate the sum of two or three arrays within the same program?

## Slide 134: Procedure Parameters (3 of 3)
ArraySum PROC
; Receives: ESI points to an array of doublewords,
; ECX = number of array elements.
; Returns: EAX = sum
;-----------------------------------------------------
  mov eax,0 ; set the sum to zero
L1: add eax,[esi] ; add each integer to sum
  add esi,4 ; point to next integer
  loop L1 ; repeat for array size
ret
ArraySum ENDP
This version of ArraySum returns the sum of any doubleword array whose address is in ESI. The sum is returned in EAX:

## Slide 135: USES Operator
Lists the registers that will be preserved
ArraySum PROC USES esi ecx
mov eax,0 ; set the sum to zero
etc.
MASM generates the code shown in gold:
ArraySum PROC
push esi
push ecx
.
.
pop ecx
pop esi
ret
ArraySum ENDP

## Slide 136: When not to push a register
SumOf PROC ; sum of three integers
  push eax ; 1
  add eax,ebx ; 2
  add eax,ecx ; 3
  pop eax ; 4
  ret
SumOf ENDP
The sum of the three registers is stored in EAX on line (3), but the POP instruction replaces it with the starting value of EAX on line (4):

## Slide 137: Program Design Using Procedures
Top-Down Design (functional decomposition) involves the following:
  design your program before starting to code
  break large tasks into smaller ones
  use a hierarchical structure based on procedure calls
  test individual procedures separately

## Slide 138: Integer Summation Program (1 of 4)
Main steps:
Prompt user for multiple integers
Calculate the sum of the array
Display the sum
Description: Write a program that prompts the user for multiple 32-bit integers, stores them in an array, calculates the sum of the array, and displays the sum on the screen.

## Slide 139: Procedure Design (2 of 4)
Main
Clrscr ; clear screen
PromptForIntegers
WriteString ; display string
ReadInt ; input integer
ArraySum ; sum the integers
DisplaySum
WriteString ; display string
WriteInt ; display integer

## Slide 140: Structure Chart (3 of 4)
gray indicates library procedure

## Slide 141: Sample Output (4 of 4)
Enter a signed integer: 550
Enter a signed integer: -23
Enter a signed integer: -96
The sum of the integers is: +431

## Slide 142: The End

## Slide 143: Copying a String
.data
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
.code
mov esi,0 ; index register
mov ecx,SIZEOF source ; loop counter
L1:
mov al,source[esi] ; get char from source
mov target[esi],al ; store it in the target
inc esi ; move to next character
loop L1 ; repeat for entire string
good use of SIZEOF
The following code copies a string from source to target:

## Slide 144: Your turn . . .
Rewrite the program shown in the previous slide, using indirect addressing rather than indexed addressing.

## Slide 145: Summary
Data Transfer
  MOV – data transfer from source to destination
  MOVSX, MOVZX, XCHG
Operand types
  direct, direct-offset, indirect, indexed
Arithmetic
  INC, DEC, ADD, SUB, NEG
  Sign, Carry, Zero, Overflow flags
Operators
  OFFSET, PTR, TYPE, LENGTHOF, SIZEOF, TYPEDEF
JMP and LOOP – branching instructions