## Slide 1
Instructor: Dr. Arbab Latif
EE-222: Microprocessor Systems
AVR Assembly

## Slide 2: Data Address Space
LDS Rd, addr ;Rd = [addr]
Example:
LDS R1, 0x60
LDS (Load direct from data space)
STS addr,Rd ;[addr]=Rd
Example:
STS 0x60,R15 ; [0x60] = R15
STS (Store direct to data space)
Example: Write a program that stores 55 into location 0x80 of RAM.
Solution:
LDI R20, 55 ;R20 = 55
STS 0x80, R20 ;[0x80] = R20 = 55
Example: Write a program that copies the contents of location 0x80 of RAM into location 0x81.
Solution:
LDS R20, 0x80 ;R20 = [0x80]
STS 0x81, R20 ;[0x81] = R20 = [0x80]
Example: Add contents of location 0x90 to contents of location 0x95 and store the result in location 0x313.
Solution:
LDS R20, 0x90 ;R20 = [0x90]
LDS R21, 0x95 ;R21 = [0x95]
ADD R20, R21 ;R20 = R20 + R21
STS 0x313, R20 ;[0x313] = R20
Example: What does the following instruction do?
LDS R20,2
Answer:
It copies the contents of R2 into R20; as 2 is the address of R2.
Solution:
LDI R20, 0x53 ;R20 = 0x53
STS 0x5E, R20 ;SPH = R20
Example: Store 0x53 into the SPH register. The address of SPH is 0x5E

## Slide 3: Data Address Space
IN Rd,IOaddress ;Rd = [addr]
Example:
IN R1, 0x3F ;R1 = SREG
IN R17,0x3E ;R17 = SPH
IN (IN from IO location)
OUT IOAddr,Rd ;[addr]=Rd
Example:
OUT 0x3F,R12 ;SREG = R12
OUT 0x3E,R15 ;SPH = R15
OUT (OUT to I/O location)
Example:
OUT SPH,R12 ;OUT 0x3E,R12
IN R15,SREG ;IN R15,0x3F
Using Names of I/O registers
Example: Write a program that adds the contents of the PINC I/O register to the contents of PIND and stores the result in location 0x90 of the SRAM
Solution:
IN R20,PINC ;R20 = PINC
IN R21,PIND ;R21 = PIND
ADD R20,R21 ;R20 = R20 + R21
STS 0x90,R20 ;[0x90] = R20