## Slide 1: Status Register (SREG)
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z
SREG:
Carry
Zero
Negative
oVerflow
Sign
N+V
Half carry
Temporary
Interrupt
H
S
V
N
C
Z
T
I
Example: Show the status of the C, H, and Z flags after the addition of 0x38 and 0x2F in the following instructions:
LDI R16, 0x38 ;R16 = 0x38
LDI R17, 0x2F ;R17 = 0x2F
ADD R16, R17 ;add R17 to R16
Solution: 1
$38 0011 1000
+ $2F 0010 1111
$67 0110 0111 R16 = 0x67
C = 0 because there is no carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 0 because the R16 (the result) has a value other than 0 after the addition.
Example: Show the status of the C, H, and Z flags after the addition of 0x9C and 0x64 in the following instructions:
LDI R20, 0x9C
LDI R21, 0x64
ADD R20, R21 ;add R21 to R20
Solution: 1
$9C 1001 1100
+ $64 0110 0100
$100 1 0000 0000 R20 = 00
C = 1 because there is a carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 1 because the R20 (the result) has a value 0 in it after the addition.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x23 from 0xA5 in the following instructions:
LDI R20, 0xA5
LDI R21, 0x23
SUB R20, R21 ;subtract R21 from R20
Solution:
$A5 1010 0101
- $23 0010 0011
$82 1000 0010 R20 = $82
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 0 because the R20 has a value other than 0 after the subtraction.
H = 0 because there is no borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x73 from 0x52 in the following instructions:
LDI R20, 0x52
LDI R21, 0x73
SUB R20, R21 ;subtract R21 from R20
Solution:
$52 0101 0010
- $73 0111 0011
$DF 1101 1111 R20 = $DF
C = 1 because R21 is bigger than R20 and there is a borrow from D8 bit.
Z = 0 because the R20 has a value other than zero after the subtraction.
H = 1 because there is a borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x9C from 0x9C in the following instructions:
LDI R20, 0x9C
LDI R21, 0x9C
SUB R20, R21 ;subtract R21 from R20
Solution:
$9C 1001 1100
- $9C 1001 1100
$00 0000 0000 R20 = $00
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 1 because the R20 is zero after the subtraction.
H = 0 because there is no borrow from D4 to D3.

## Slide 2: .INCLUDE
.INCLUDE “filename.ext”
.equ SREG = 0x3f
.equ SPL = 0x3d
.equ SPH = 0x3e
....
M328def.inc
LDI R20, 10
OUT SPL, R20
Program.asm