## Slide 2: Charge
All matter consists of atomic particles.
Charge is an electrical property of the atomic particles.
Unit of measure of charge is coulomb ‘C’ (Coulomb 1736 – 1806).
Charge ‘e’ of an electron is negative & equal in magnitude to 1.602 X 10-19 C. Concurrently, a single proton has a charge of + 1.602 X 10-19 C.
One coulomb of charge is present on 1 / 1.602 X 10-19 electrons. This is equal to 6.24 X 1018 electrons.
Charge is represented by ‘Q’ (time-invariant) and q(t) or ‘q’ when it varies with time.
Law of conservation of charge states that charge can neither be created nor destroyed.
Current !

## Slide 3: Current
A unique feature of charge is that it is mobile.
Charge in motion is called electric current represented by ‘I’ or i(t) or ‘i’.
When force is applied or work is done, negative charges can be made to move in one direction while the positive charges can be made to move in the opposite direction, thus constituting a current.
It is conventional to take current flow as movement of positive charges (Benjamin Franklin 1706 – 1790).
A convention is a standard way of describing something so that others in the profession can understand.
Mathematically current ‘i’ and charge ‘q’ are related by :-
    i = dq / dt where current ‘i’ is measured in amperes (A)
    So 1 ampere = 1 coulomb / second
If the current does not change with time, we call it direct current (dc).
An alternating current (ac) is, conventionally, a current that varies sinusoidally with time.
AC and DC Current.

## Slide 4: AC & DC Current
Example of charge & current !
Exponential and damped sinusoid currents!!
t
i
A unidirectional current is called dc or direct current.
Alternating current (ac) is current that changes direction cyclically.
t
i

## Slide 5
2
4
6
8
t (s)
q (C)
50
- 50
Example : Charge & Current
The charge flowing in a wire is plotted as follows; sketch the corresponding current.
Notes: At t = 1 sec the charge q(1) is measured as 25 coulomb. So between 0 sec and 1 sec the charge flow is 25 coulomb in 1 sec; hence current i(1) = 25 A.
  Again at t = 7 sec the charge is q(7) = - 25 A. From q(6) of – 50 A the change is final value – initial value that is – 25 – (- 50) = 25 so i(7) = 25 A.
…contd.

## Slide 6
2
4
6
8
t (s)
i (A)
25
- 25
2
4
6
8
t (s)
q (C)
50
- 50
Voltage !
Example : Charge & Current ….contd

## Slide 7: Voltage
The energy needed to move a unit charge from one point to another is called voltage or potential difference or electromotive force (emf).
  So vab is the energy (or work) needed to move a unit charge from point ‘a’ to ‘b’.
Energy is the capacity to do work.
  The fundamental unit of work or energy is the joule (J).
Mathematically, the relationship is :-
  vab = dw / dq where ‘w’ is energy in joules (J) & ‘q’ is charge in coulombs.
  So 1 volt = 1 joule / coulomb
  a b
  + -
Note current is related to the charge flowing through a circuit element whereas voltage is a measure of potential energy difference across the element.
…. contd.

## Slide 8: Voltage…contd
Pushing charge or sending current through one end (terminal) and out another requires an expenditure of energy or work to be done. We say a potential difference or an electrical voltage exists between the two terminals.
Voltage cannot be defined at a single point; it is by definition the difference in potential between two points.
Electric current is always through an element and voltage is always across the element or between two points.
Any question !

## Slide 9
He who asks a question
is a fool for five minutes; he who does not ask a question
remains a fool forever.
(Chinese proverb)

## Slide 10: Voltage : additional notes
One joule of work is done when a force of one newton moves an object through one meter. So W = F X d
The force is one newton when a mass of one kg is moved at the rate of one meter per sec per sec.
  The fundamental unit of force is newton (N).