## Slide 2: Power
Power is defined as the rate at which work is done or energy is expended.
Energy is the capacity to do work. The fundamental unit of work or energy is the joule (J).
Power is expressed in watts (W). Power is one watt if one joule of energy is expended in transferring one coulomb of charge through the device in one second.
One joule of work is done when a force of one newton moves an object through one meter.
The force is one newton when a mass of one kg is moved at the rate of one meter per sec per sec.
So W = F X d
Mathematically, the relationship is :-
  p = dw / dt
  where ‘p’ is power in watts (W), ‘w’ is energy in joules (J) & ‘t’ is time in seconds.
Also p = dw / dt = dw / dq X dq / dt = vi
where dw / dq is the voltage (energy required to move a unit charge)
Note : 1 joule = 1 watt - 1sec (dw = p dt) and
3600 J = 1 watt – 3600 sec or 1 Wh
Example !

## Slide 3: Example : Power
Passive Sign Convention !
How much energy does a 100 - watt electric bulb consume in two hours?
We know p = dw / dt where w is in joules and t in seconds.
So 100 = w (joules) / (2X60X60)
Hence w = 720 k joules.
Also pdt = dw
So watt X sec = joules
Or watt X 3600 X sec = joules X 3600
Hence 1watt-hour = 3600 joules
And 100 watt - hr = 360 k joules (watt-hr is the unit used by electrical companies)
And in 2 hours : 200 watt - hr = 720 k joules QED

## Slide 4: Passive Sign Convention
The passive sign convention is satisfied when the current arrow is directed into the element at the plus - marked terminal.
It says (the passive sign convention) that if the current arrow and the voltage polarity signs are placed such that the current enters that end of the element marked with the positive sign, then the power absorbed can be expressed by the product of the specified current and voltage variables.
  If the numerical value of the product is negative, then we say that the element is absorbing negative power, or that it is actually generating power (and delivering it to some external element).
    In the first case the +ve terminal is at 5 volts wrt the other terminal.
    In the second case the +ve terminal is at – 5 volts wrt the other terminal.
The Circuit Elements !
+
_
_
_
+
+
5 V
- 5 V
5 V
3 A
- 3 A
- 3 A
15 w
(absorbed)
15 w
(absorbed)
-15 w
(absorbed)
15 w
(generated)
OR

## Slide 5: The Circuit Elements
Each component of the circuit is called an element.
The circuit elements can be described as :-
  Active elements and
  Passive elements
Voltage sources and current sources are classified as active elements. These are capable of delivering power to some external device.
Passive elements include resistors, capacitors and inductors.
Incidentally, the voltage – current relationship is :-
  V∞i , V∞∫idt , V∞di /dt
An ideal (?) independent source is an active element that provides a specific voltage or current that is completely independent of other circuit variables.
Voltage & Current Sources !

## Slide 6: Independent Voltage Sources
The symbols for independent voltage sources are:-
Small ‘v’ is used for time varying or constant voltages.
Capital ‘V’ is used for constant voltages only.
Independent current sources !
v
+
_
V
+
_
or
V
+
_

## Slide 7: Independent Current Sources
The symbols for independent current sources are:-
Small ‘i’ is used for time varying or constant currents.
Capital ‘I’ is used for constant currents only.
Note: Do not think that the voltage across the current source is zero. IT SHALL DEPEND ON THE CIRCUIT TO WHICH IT IS CONNECTED.
Dependent ( or controlled) Sources !
i
I

## Slide 8: Dependent Sources
The symbols for dependent voltage sources are:-
  Voltage controlled voltage source has ‘k’ which is a dimensionless scaling constant.
  Current controlled voltage source has a scaling constant ‘r’ with units of V/A.
Dependent sources …contd !
An ideal dependent (or controlled) source is an active element in which the source quantity is controlled by another voltage or current existing in the circuit being analyzed.
kvx
+
_
rix
+
_
There are four types of dependent sources :-
  A voltage controlled voltage source.
  A current controlled voltage source.
  A voltage controlled current source.
  A current controlled current source.

## Slide 9: Dependent Sources…contd
The symbols for dependent current sources are:-
Current controlled current source has a scaling constant ‘k’ which is a dimensionless scaling constant.
Voltage controlled current source has a scaling constant ‘g’ which has units of A/V.
Example dependent source !
kix
gvx

## Slide 10: Dependent Source : DC Equivalent Model of a Transistor
This is the symbol of a transistor.
The dc equivalent model of the transistor.
Networks & Circuits !
IB
B
C
E
IB
βIB
B
C
E

## Slide 11: Networks & Circuits
Network : interconnection of two or more elements
Circuit : a network providing one or more closed paths
Active Network : contains active element
Passive Network : no active element
  Networks have branches, nodes, paths, loops and meshes etc.
Ohm’s Law !

## Slide 12: Ohm’s Law
Relationship between current and voltage for a resistor : found in 1827 by Ohm (German physicist 1787 – 1854)
Forty-six years earlier Henry Cavendish, a semi recluse, had also discovered this relationship.
Ohm’s Law states that the voltage ‘v’ across a resistor is directly proportional to the current ‘i’ flowing through the resistor
Mathematically,
v ∞ i
Ohm defined constant of proportionality as ‘R’, resistance
        So v = iR where ‘R’ is in ohms (Ω)
Ohm’s Law…contd!
R
i
+
_
v

## Slide 13: Ohm’s Law/Power Absorption/Conductance
A resistor that obeys Ohm’s law is a linear resistor.
Resistance is normally a positive quantity, although negative resistance may be simulated with special circuitry.
Power Absorption :
We know : p = vi = i2 R = v2/R
The absorbed power appears as heat/light and is always positive.
An element supplies positive power if positive current flows out of the positive voltage terminal. An element absorbs positive power if positive current flows into the positive voltage terminal.
Conductance :
Another useful quantity in circuit analysis is reciprocal of resistance ‘R’, known as conductance and denoted by ‘G’ where
  G = 1/R = i/v
  unit is mho (inverted omega)
  The SI unit is siemens 1S = 1 = 1 A/V
The Resistor !
Ω
Ω
Slope R
v
i
Slope R
changing
v
i

## Slide 14: The Resistor
For the material shown,
    R ∞ l
    R ∞ 1 / A
    So R = ρ (l / A)
    Where ρ is resistivity in ohm – meters.
Resistivity is the measure of the ease with which electrons can travel through a material. High resistivity means greater difficulty, more resistance.
Silver has 1.64 X 10 - 8 Ω – meter : conductor
Silicon has 6.4 X 10 2 Ω - meter : semi conductor
Paper has 1010 Ω - meter : insulator
In general, materials resist the flow of electric charge.
This physical property or ability to resist current is known as resistance and is represented by symbol ‘R’.
The circuit symbol for resistance is :-
Resistor is the simplest passive element. It always absorbs power from the circuit.
Colour coding and power dissipation.
Nodes, Paths, Loops & Branches !
Length ‘l’
A
ρ
R
R
R

## Slide 15
We cannot change the direction of the wind, but we can adjust the sails.
(Anonymous)