## Slide 2: Nodes, Paths, Loops, and Branches
Network topology means the ups and downs or the characteristics of the network.
A point at which two or more elements have a common connection is called a node.
If no node was encountered more than once then the set of nodes and elements that we traverse is called a path.
If the node at which we started is the same node at which we ended, then the path is, by definition, a closed path or a loop.
….contd
b
+
_
R
R
R
V
I
a
c

## Slide 3: Network Topology….contd
A branch is defined as a single path in a network, composed of one simple element and the node at each end of that element. (No element : no branch)
A mesh is a loop which does not contain any other loops within it.
Two or more elements are in series if they are cascaded or connected sequentially and consequently carry the same (not identical) current.
Two or more elements are in parallel if they are connected to the same two nodes & consequently have the same voltage across them.
KCL and KVL.
b
+
_
R
R
R
V
I
a
c

## Slide 4: Kirchhoff’s Laws
Kirchhoff was a German professor (1824 – 1887).
Ohm’s Law alone could not solve all issues pertaining to circuit analysis.
Kirchhoff, in 1847, stated that “algebraic sum of all the currents entering a node (or a closed boundary) is equal to zero.”
This law is based on the law of conservation of charge.
Law of conservation of charge.
ia
ic
ib
id
ia + ib +(- ic)+ id = 0
ia
ic
ib
id
ia
ic
ib
id
ia
ic
ib
id
ia
ic
ib
id
∑ in = 0
n = 1
N

## Slide 5: Law of Conservation of Charge
Charge can be transferred from one object to another. The algebraic sum of charge on the two objects will be the same before and after the transfer. This is sometimes called the Law of Conservation of Charge, discovered by Benjamin Franklin (1706 – 1790).
Kirchhoff’s Laws.

## Slide 6: Kirchhoff’s Laws
Kirchhoff also stated that “algebraic sum of all the voltages around a closed path (or loop) is equal to zero.”
This law is based on the law of conservation of energy.
The energy required to move a unit charge from point A to point B in a circuit is independent of the path taken from A to B.
Application of KVL:
  Follow a clockwise direction.
  Write down the voltage of each element whose positive terminal is entered.
  Write down negative of every voltage first met at the negative sign.
Law of Conservation of Energy.
A
B
-
+
+
-
-
+
V1
V2
V3
-V1 + V2 –V3 = 0
∑ Vn = 0
n = 1
N

## Slide 7: Law of Conservation of Energy
It states that the total inflow of energy into a system must equal the total outflow of energy from the system, plus the change in the energy contained within the system. In other words, energy can be converted from one form to another, but it cannot be created or destroyed.
(German surgeon Mayer in 1842 and Joule in 1843 discovered the law)
  Note: It is often erroneously thought that ”the current takes the path of least resistance”, whereas it simply divides in keeping with the three circuit laws. There is no way that an ‘intelligent’ current looks ahead and then decides what rout to take.
Examples !

## Slide 8: Example : KCL
For the circuit, compute the current through resistor R3 if the voltage source supplies a current of 3 A.
…contd!
5 A
+
_
R1
R3
R2
10 V
2 A

## Slide 9: Example : KCL….contd
Label the current through R3 and R1 as i and iR1 respectively.
Identify a node at the right top of the circuit.
Apply KCL at the node and write :
      iR1 + (-2) + (-i) + 5 = 0
      iR1 – i + 3 = 0
      So i = 3 + iR1
Given iR1 = 3A
Therefore i = 3 + 3 = 6 A.
Example KVL.
5 A
+
_
R1
R3
R2
10 V
2 A
i
iR1
5 A
+
_
R1
R3
R2
10 V
2 A

## Slide 10: Example : KVL
Determine vX.
…contd !
ix
+
_
30 V
8 Ω
10 Ω
2 Ω
2 Ω
+
-
vx
2 A

## Slide 11: Example : KVL…contd
KCL at node ‘a’ yields : i2 + ix = iy
KVL for 1st closed path : 30 = 8 X 2 + v10 or v10 = 14
Then i10 = 14/10 = 1.4 Hence i2 = 2 – 1.4 = 0.6 A and v2 = 2 x 0.6 = 1.2 v
Applying KVL to middle loop : v10 = v2 + vy or 14 = 1.2 + vy
Therefore vy = 12.8 and so iy = 12.8/2 = 6.4
Finally vx = 2 X iy = 2 X 6.4 = 12.8 volts.
Another Example !
a
ix
+
_
vy
30 V
i2
8 Ω
i10
10 Ω
2 Ω
2 Ω
iy
+
-
+
+
+
-
-
-
-
vx
v10
v8
v2
2 A
30 V
+
_
8 Ω
10 Ω
2 Ω
2 Ω
+
-
vx
2 A
ix

## Slide 12: Another Example : Dependent Sources
Calculate vy.
vX = 5 V therefore 3vX = 15 A
The current thru 1 ohm is 15 – 3 = 12 A
So vY = 12 volts QED
Yet Another Example !
+
_
5 V
vx
+
-
3vx
3 A
2 Ω
1 Ω
vy
+
-

## Slide 13: Yet Another Example
If iX = 5 A find v1 and iY. (All resistances are in ohms)
With iX = 5 A therefore iS = 5 A
The voltage across the two resistors is the same so equal amount of current flows through each.
So iv1 = 2.5 A and therefore v1 = 25 volts
Also iY = 2.5 A
The Single Loop Circuit !
i S
10
10
10
10
v1
-
+
iY
iX

## Slide 14: The Single Loop Circuit
We know Ohm’s Law and Kirchhoff’s Laws.
Consider the following circuit :
+
_
_
_
+
_
R2
R1
vS1
vS2
Note no additional information like given current through a particular element etc is given.
We analyze this single loop circuit ie:
  Determine voltage across each element
  Determine current through each element and
  Power absorbed by each element
Contd!

## Slide 15: The Single Loop Circuit …contd
Step 1 : Arbitrarily select a clockwise current i as shown :
Note: All the elements in a circuit that carry the same current are said to be connected in series.
Contd !
+
_
_
_
+
_
R2
R1
vS1
vS2
i
i
+
_
+
_
R2
R1
vS1
vS2

## Slide 16
Step 2 : Where current enters the element, label the terminal as positive.
Step 3 : Apply KVL (again going in the clockwise direction) :
- vS1 + vR1 + vS2 + vR2 = 0
Applying Ohm’s Law to resistive elements :
vR1 = R1 i and vR2 = i R2
So we get : i = ( vS1 – vS2 ) / ( R1 + R2 )
Voltage and Power can be found by v = Ri, p = vi or p = i2R
The Single Loop Circuit : Power Example!
+
_
_
_
+
_
R2
R1
vS1
vS2
i
i
+
+
-
-
The Single Loop Circuit …contd

## Slide 17
Step 1 : Assign a ref direction for current i and ref polarity for v30.
Step 2 : Apply KVL
- 120 + v30 + 2 vA – vA = 0
Step 3 : Use Ohm’s law
v30 = 30 i and vA = - 15 i
Step 4 : Put these values in first equation and solve for i.
We get i = 8 A Therefore vA = - 120 V
Hence P 120v = - 960 W and P30 = 1920 W and P 2vA = - 1920 W and P15 = 960 W
Notice the power sources are supplying power and resistors are absorbing power.
Compute the power absorbed in each element.
+
30 Ω
2vA V
15 Ω
+
_
vA
+
_
120 V
i
The Single Loop Circuit …Power Absorbed

## Slide 18: Software for Circuit Analysis
PSPICE is a computer software circuit analysis program. PSPICE for windows can be used to analyze circuits. It is an abbreviation of Simulation Programme with Integrated – Circuit Emphasis.
MATLAB is an abbreviation for MATrix LABoratory. It has become a powerful tool of technical professionals worldwide. It is a computational tool that uses matrices and vectors to carry out numerical analysis, signal processing and scientific visualization tasks.

## Slide 19: An Over-Simplified Indigenous Model
STUDENTS/FACULTY
INTRINSIC MOTIVATION
COMMITED STUDENTS/FACULTY
DEVELOPMENT PROGRAMS
QUALITY IN HIGHER EDUCATION
FRUSTRATION
NOBLE
PROFESSION
LOYALTY
TO INSTITUTION
TO
EXCEL
TRAINING
ISSUES
CHALLENGES

## Slide 20
Traveler, there are no roads. Roads are made by walking.
(Spanish proverb)