## Slide 2: The Single Node - Pair Circuit
Step 1 : Assume a voltage across any element assigning an arbitrary polarity as shown.
Note : Elements in a circuit having a common voltage across them are said to be connected in parallel.
….contd !
120 A
1/30 Ω
1/15 Ω
30 A
+
v1
-
In a single node – pair circuit, any number of simple elements are connected between the same pair of nodes.

## Slide 3: The Single Node-Pair Circuit….contd
Step 2 : Having chosen voltage polarity, i1 and i2 are labeled from positive to negative.
120 A
1/30 Ω
1/15 Ω
30 A
+
v1
-
i1
i2
Step 3 : Applying KCL :
120 – i1 – 30 – i2 = 0 ------------ A
Now i = v / R gives us i1 = 30v1 and i2 = 15 v1 thus A becomes :
120 – 30v1 – 30 – 15v1 = 0
So v1 = 2 volts and i1 = 60 A and i2 = 30 A
…contd !

## Slide 4
With v1 = 2 volts and R1 = 1/30 and R2 = 1/15 ohms
For power calculations V2/R :
  PR1 = 30 (2)2 = 120 W and
  PR2 = 15 (2)2 = 60 W
For the two sources :
  P120A = 120 ( - 2 ) = - 240 W (Current entering –VE TO + VE)
  P30A = 30 ( 2 ) = 60 W (Current entering +VE TO –VE)
Note : 120 A source is delivering power and 30 A source is absorbing power.
Total power is equal to zero.
Recall current coming out of +ve terminal of a battery and thus the source is delivering power.
Examples !
-
120 A
1/30 Ω
1/15 Ω
30 A
+
v1
i1
i2
The Single Node-Pair Circuit….contd

## Slide 5: Example : KCL
Find the power absorbed by 8A source.
Examples….contd !
So v1/4 + v1/6 + v1/12 = 8 + 7 and v1 = 30 volts
Hence P8A = 240 watts (generated)
6 Ω
7 A
4 Ω
12 Ω
8 A
M
N
8 A
V1
+
_
12 Ω
4 Ω
7 A
6 Ω
N
M
How to proceed??

## Slide 6: Example : KCL
Find the labelled currents.
So KCL at top node: i1 + 0.2v1 +i2 – i10 – 2.5 = 0 and i10 = v1 /10 etc etc
Hence v1 = 50 volts and the currents can be determined and verified by KCL.
V1
+
_
10Ω
0.2v1
25 Ω
25 A
100 Ω
i1
i2
A
B
C
D
V1
+
_
100 Ω
25 Ω
25 A
10 Ω
0.2v1
A
A
B
D
C
i1
i2
i10
Solution!
Series and Parallel Connected Independent Sources !

## Slide 7: Series & Parallel Connected Sources
Several voltage sources in series may be replaced by an equivalent voltage source having a voltage equal to the algebraic sum of individual sources.
+
_
+
_
+
_
v1
v2
v3
OR
+
_
_
_
V1 + V2 – V3
Ideal voltage sources in parallel are permissible only when each has the same terminal voltage (not for extended period of time).
In case of two sources in parallel, each will supply half the current.
And large current flows in closed loop for different voltage sources (due to low 0.05 ohm resistance of each) in parallel.
Current Sources !

## Slide 8: Series & Parallel Connected Sources....contd
Several current sources in parallel may be replaced by an equivalent current source having a current equal to the algebraic sum of individual sources.
Ideal current sources in series are permissible only when each has the same current and direction.
Example !
i1 - i2 + i3
OR
i1
i2
i3

## Slide 9: Example : Series & Parallel Connected Sources
Find v1 ?
Solution !
12 mA
V1
+
_
.03 Vx A
1 kΩ
Vx
+
_
10 kΩ
3.5 mA
1 mA
- 3 mA

## Slide 10: Example : …contd
So vX = - 2 volts
Solution…contd !
12 mA
V1
+
_
.03 Vx A
1 kΩ
Vx
+
_
10 kΩ
3.5 mA
1 mA
- 3 mA
Vx
+
_
- 2 mA
1 kΩ
Vx
+
_
2 mA
1 kΩ
=

## Slide 11: Example : ….contd
So i = 12 – 3.5 – 60 = – 51.5 mA and v1 = – 515 volts because :
Resistors !
12 mA
V1
+
_
.03 Vx = - .06 A
1 kΩ
Vx
+
_
10 kΩ
3.5 mA
1 mA
- 3 mA
12 mA
V1
+
_
10 kΩ
3.5 mA
- 60 mA
i
R
i
+
_
v

## Slide 12: Resistors In Series & Parallel
For circuit analysis, complicated resistor combinations can be replaced by a single resistor.
Consider the following circuit :
Step 1 : Apply KVL so vS = v1 + v2 + v3
Step 2 : Apply Ohm’s Law so vS = iR1 + iR2 + iR3
Contd !
+
_
_
_
R3
R1
vS
R2
i
v1
v2
v3
+
+
+
_
_
_

## Slide 13: Resistors In Series
So vS = iReq
And iReq = iR1 + iR2 + iR3
Therefore Req = R1 + R2 + R3
Generalizing Req = R1 + R2 + R3 + …… RN
Resistors in series are simply added together to determine equivalent resistance.
Resistors in Parallel !
+
_
Req
vS
i
+
_
R3
R1
vS
R2
i
v1
v2
v3
+
+
+
_
_
_

## Slide 14: Resistors in Parallel
Step 1 : Apply KCL so iS = i1 + i2 + i3
Step 2 : Apply Ohm’s Law so iS = v/R1 + v/R2 + v/R3
So iS = v/Req = v/R1 + v/R2 + v/R3
And 1/Req = 1/R1 + 1/R2 + 1/R3
Also Geq = G1 + G2 + G3
Note that the reciprocal of the equivalent resistance is equal to the sum of the reciprocals of the individual resistances connected in parallel.
Also note: R1 // R2 = R1 R2 /(R1 + R2)
Examples !
R3
iS
R2
R1
iS
i1
i2
i3
v
+
_
Req
iS
V
+
_

## Slide 15: Examples : Series & Parallel Resistances
Find Rab for the circuit? All resistances are in ohms.
Examples !
Step 1 : 20 // 5 = 4
Step 2 : 1 + 4 = 5
Step 3 : 20 // 5 = 4
Step 4 : 2 + 4 = 6
Step 5 : 6 // 9 = 3.6
Step 6 : 18 // 3.6 = 3
So R = 3 + 8 = 11 Ω
18
a
b
20
8
5
20
1
9
2

## Slide 16: Examples : Series & Parallel Resistances
Find Rab for the circuit? All resistances are in ohms.
Voltage Division !
Rab = 24 Ω
a
b
3
8
10
5
20
6

## Slide 17: Voltage Division
This is another useful tool for circuit analysis.
Voltage division is used to express the voltage across one of several series resistors in terms of the voltage across the combination.
Consider the following circuit :
Applying KVL :
v = v1 + v2 = iR1 + iR2 = i (R1 + R2)
So i = v / (R1 + R2)
Now v2 = iR2 = vR2 / (R1 + R2)
Or v2 = {R2 / (R1 + R2)  v
And v1 = {R1 / (R1 + R2)  v
Generalizing :
vk = {Rk / (R1 + R2+…RN)  v
where R1 through RN are resistances in series.
Derivation!
R2
R1
v1
v2
+
+
_
_
v
+
_
i

## Slide 18: Voltage Division : Derivation
Solution:
  VSI = I2R1 + I2R2
  Or VS = IR1 + IR2 (dividing by I)
  Now VR2 = IR2
  And I = VS /(R1 + R2)
  Hence VR2 can be determined.
Current Division !
Using the fact that total power supplied is equal to total power absorbed, show that :
VR2 = VS
R2
R1
+
R2
+
_
_
_
R2
vS
I
R1
+
-

## Slide 19: Current Division
R2
R1
i
i1
i2
v
+
_
Current division is used to express the current through one of several parallel resistors in terms of the current through the combination.
Now v = i2R2
So i2 = v / R2 = i (R1 // R2)
R2
Because v = i (R1 // R2)
And i2 = i/R2 {R1R2/(R1 + R2)}
So i2 = i {R1/(R1 + R2)}
And i1 = i {R2/(R1 + R2)}
Example !
Nodal Analysis !

## Slide 20
Great heights reached by men and kept,
Were not attained by sudden flight,
But they while their companions slept,
Were toiling upward in the night.
(Anonymous)