## Slide 2: Mesh Analysis
An alternative method : Mesh Analysis
Loop : A closed path
Mesh : A loop that does not contain any other loops within it.
Consider the following circuit :
The circuit has two meshes (and three loops).
Mesh current : Current that flows around the perimeter of a mesh.
Contd !
3 Ω
6 Ω
+
-
42 V
4 Ω
+
-
10 V
i2
i1

## Slide 3: Mesh Analysis…contd
Applying KVL to mesh 1:
    - 42 + 6 i1 + 3 ( i1 – i2 ) = 0
And KVL to mesh 2 yields :
3 ( i2 – i1 ) + 4 i2 - 10 = 0
The two equations can be simplified as follows :
- 3 i1 + 7 i2 = 10
9 i1 - 3 i2 = 42
So i1 = 6 A and i2 = 4 A
Supermesh !
3 Ω
6 Ω
+
-
42 V
4 Ω
+
-
10 V
i2
i1

## Slide 4: The Supermesh
What happens when a current source is present in the network? To apply KVL, voltage across current source is not known.
Consider the following circuit :
Here we create a “ supermesh “ from two meshes that have a current source as a common element : the current source is in the interior of the supermesh.
If a current source lies on the periphery of a mesh, no KVL equation is needed and the mesh current is determined by inspection. This is similar to the voltage sources connected to the reference terminal.
Note that a supermesh results when two meshes have a current source (dependent or independent) in common.
…contd !
_
7 V
2 Ω
3 Ω
7 A
+
1 Ω
2 Ω
1 Ω
i1
i2
i3

## Slide 5: The Supermesh…contd
A supermesh has no current of its own.
The current source in the supermesh provides the constraint equation necessary to solve for mesh currents.
A supermesh requires application of both KVL and KCL.
Applying KVL meshes 1 and 3 (as a supermesh)
- 7 + 1 (i1 – i2) + 3 (i3 – i2) + 1 (i3 ) = 0
And mesh 2 1 (i2 – i1) + 2 i2 + 3 (i2 – i3) = 0
Applying KCL to branch containing current source provides us i1 – i3 = 7
SOLUTION i1 = 9 A i2 = 2.5 A i3 = 2 A
_
7 V
2 Ω
3 Ω
7 A
+
1 Ω
2 Ω
1 Ω
i1
i2
i3
Mesh Equations : Any Circuit !

## Slide 6: Mesh Equations : Any Circuit
The procedure :
  Ensure network is a planar network.
  Indicate all element and source values with reference symbols.
  With M meshes, assign a clockwise mesh current in each mesh : i1, i2 ……iM.
  Apply KVL around each mesh.
  For current sources, create a supermesh. Assigned mesh currents should not be changed.
  Write down the mesh equations and solve them.
…contd !

## Slide 7: Mesh Equations : Any Circuit
Mesh analysis is not applicable to non – planar networks.
Non – planar networks are those that cannot be drawn on a plane surface without a branch passing over or under any other branch.
The End !
a
b
c
d

## Slide 8: The important thing about a problem is not its solution but the strength we gain in finding the solution. (Anonymous)