## Slide 2: Linearity and Superposition
A linear element is defined as a passive element that has a linear voltage – current relationship.
Linear relationship means that for v(t) = R i(t), we have k v(t) = k R i(t),
The plot of v – i relationship results in a straight line.
A linear circuit is defined as a circuit composed entirely of independent sources, linear dependent sources and linear elements.
The superposition principle !
v (t)
i (t)
Slope = 1/R
dv/dt
i (t)
Slope = C
di/dt
v (t)
Slope = L

## Slide 3: The Superposition Principle
Most important consequence of linearity is superposition.
The principle of superposition states that :
  “ the response (a desired current or voltage) in a linear circuit having more than one independent source can be obtained by adding the responses caused by the separate independent sources acting alone.”
  If we reduce a voltage source to zero volts, we have effectively created a short circuit.
  If we reduce a current source to zero amps, we have effectively created an open circuit.
The Superposition Theorem !
+
_

## Slide 4: The Superposition Theorem
The superposition theorem states :-
  In any linear resistive network, the voltage across or the current through any resistor or source may be calculated by adding algebraically all the individual voltages or currents caused by the separate independent sources acting alone, with all other independent voltage sources replaced by short circuits and all other independent current sources replaced by open circuits.
    Superposition is also extremely useful when dealing with a circuit in which not all sources operate at the same frequency.
Treatment of dependent sources ?
Example !

## Slide 5: Example : Superposition
Using superposition, find ix ?
Contd !
9 Ω
6 Ω
2 A
+
_
_
_
3 V
ix

## Slide 6: Example…contd
Step 1 : Set current source equal to zero.
Contd !
9 Ω
6 Ω
+
_
_
_
3 V
ix(3v)
So
ix(3v) = 3/15 = 0.2 A
2 A
9 Ω
6 Ω
+
_
3 V
ix

## Slide 7: Example : …contd
Step 2 : Set voltage source equal to zero.
Therefore ix = 0.2 + 0.8 = 1 A
Treatment of power calculations ?
Examples !
So
ix(2A) = { 6/(6 + 9)2 = 6/15 X 2 = 0.8 A
9 Ω
6 Ω
2 A
ix(2A)
2 A
9 Ω
6 Ω
+
_
3 V
ix

## Slide 8: We should not write so that it is possible for the reader to understand us; but so that it is impossible for him to misunderstand us. (Quintilian)