## Slide 2: Thevenin Equivalent Circuit
The Equivalent Circuits!
In circuit analysis, sometimes a situation may arise like shown :
Complex network
RL
M. L. Thevenin’s (1883) theorem states that it is possible to replace everything except the load resistor by an independent voltage source in series with a resistor.
A corollary, E. L. Norton’s (1926) theorem states that we obtain an equivalent circuit composed of an independent current source in parallel with a resistor.
Usefulness.

## Slide 3: Equivalent Circuits
Thevenin’s Theorem !
The two equivalent circuits are :
+
_
VTh
RTh
RL
iN
RN
RL

## Slide 4: Thevenin’s Theorem
Example !
When obtaining Thevenin or Norton equivalent of complex circuits, we use Thevenin’s theorem that states:
  “ Given any linear circuit, rearrange it in the form of two networks A and B connected by two wires. Define a voltage vOC as the open circuit voltage which appears across the terminals of A when B is disconnected. Then all currents and voltages in B will remain unchanged if all independent voltage and current sources in A are killed or zeroed out, and an independent voltage source vOC is connected with proper polarity, in series with the dead (inactive) A network. “

## Slide 5: Example : Thevenin’s Theorem
Another Example !
Given the circuit :
+
_
6 Ω
12 V
+
_
RL
7 Ω
3 Ω
A
B
Step 1 : RL is disconnected.
Step 2 : vOC = (6/9) X 12 = 8 volts
Step 3 : Zeroed network (killed network)
6 Ω
7 Ω
3 Ω
So Thevenin equivalent resistance = 3 // 6 + 7 = 2 + 7 = 9
and
8 V
+
_
RL
9 Ω
Dependent Sources !

## Slide 6: Another Example : Thevenin’s Theorem
General Strategy !
Given a linear circuit as shown. When a 10 kΩ resistor is connected to terminals a – b, the voltage Vab is measured as 6 volts. When a 30 kΩ resistor is connected to the terminals, the voltage Vab is measured as 12 volts. Determine the Thevenin equivalent at terminals a and b. Also find Vab when a 20 kΩ resistor is connected to terminals a and b.
a
Linear network
b
Solution:
  Determine current through 10 kΩ resistor as 6/10 = 0.6 mA
  So VTh = 0.6 RTh + 6
  Also current through 30 kΩ resistor is 12/30 = 0.4 mA
  So VTh = 0.4 RTh + 12
  RTh can be found as 30 kΩ
  And VTh as 24 volts.
  Vab when a 20 kΩ resistor is connected to terminals a – b is 9.6 volts.

## Slide 7: General Strategy for Thevenin’s Theorem
Best of Luck !
Remove the load and find the voltage Voc across the open circuit terminals using any of the circuit analysis techniques.
Determine the Thevenin equivalent resistance of the network at the open terminals with the load removed :
  If the circuit contains only independent sources, they are made zero. RTh is found by computing the resistance of the purely resistive network at the open terminals.
  If the circuit contains only dependent sources, an independent voltage or current source is applied at the open terminals and the corresponding current or voltage at these terminals is measured. The voltage/current ratio at the terminals is the Thevenin equivalent resistance.
  (Note: Since there is no energy source, the open-circuit voltage is zero in this case.)
  If the circuit contains both independent and dependent sources, the open circuit terminals are shorted and the short-circuit current between these terminals is determined. The ratio of the open-circuit voltage to the short-circuit current is the resistance RTh.

## Slide 8
People of accomplishment rarely sat back and let things happen to them.
They went out and happened to things.
(Leonardo Da Vinci)