## Slide 2: Norton’s Theorem
Example !
Proposed in 1926, 43 years after Thevenin’s Theorem, by E. L. Norton, an American Engineer at Bell Telephone Laboratories.
It states:
  “Given any linear circuit, rearrange it in the form of two networks A and B connected by two wires. If either network contains a dependent source, its control variable must be in that same network. Define a current Isc as the short circuited current that appears when B is disconnected and the terminals of A are short circuited. Then all currents and voltages in B will remain unchanged if all independent voltage and current sources in A are killed or zeroed out, and an independent current source Isc is connected, with proper polarity, in parallel with the dead (inactive) A network.”
So Norton equivalent of a linear network is the Norton current source Isc in parallel with the Thevenin resistance RTh.
Also source transformation on Thevenin equivalent yields Norton’s equivalent.
And voc = RThIsc

## Slide 3: Example : Norton’s
…Contd !
Given the circuit :
+
_
2 mA
4 V
+
_
3k Ω
2k Ω
1k Ω
+
_
2 mA
4 V
+
_
3k Ω
2k Ω
1k Ω

## Slide 4: Example : Norton’s…contd
…Contd !
Making two separate networks:
Step 1 : Find isc.
+
_
2 mA
4 V
+
_
3k Ω
2k Ω
A
B
1k Ω
+
_
2 mA
4 V
+
_
3k Ω
2k Ω
isc
So isc = 4/(2+3) + 2/(2+3) X 2 = 0.8 + 0.8 = 1.6 mA

## Slide 5: Example : Norton’s …contd
General Strategy!
Step 2 : Find RTh .
3k Ω
2k Ω
RTh
So RN = RTh = 5k Ω
5k Ω
1.6 mA
1k Ω
+
_
2 mA
4 V
+
_
3k Ω
2k Ω

## Slide 6: General Strategy for Norton’s Theorem
Maximum Power Transfer Theorem!
Remove the load and find the current Isc across the open circuit terminals using any of the circuit analysis techniques.
Determine the Norton (or Thevenin) equivalent resistance of the network at the open terminals with the load removed :
  If the circuit contains only independent sources, they are made zero. RN (or RTh) is found by computing the resistance of the purely resistive network at the open terminals.
  If the circuit contains only dependent sources, an independent voltage or current source is applied at the open terminals and the corresponding current or voltage at these terminals is measured. The voltage/current ratio at the terminals is the Norton (or Thevenin) equivalent resistance. (Note: Since there is no energy source, the short-circuit current is zero in this case.)
  If the circuit contains both independent and dependent sources, the open circuit terminals are shorted and the short-circuit current between these terminals is determined. The ratio of the open-circuit voltage to the short-circuit current is the resistance RN (or RTh) .

## Slide 7: Small things make perfection but perfection is no small thing.
(Anonymous)