## Slide 2: Maximum Power Transfer Theorem
So
In most applications, circuit analysis demands that power delivered to the load be maximized.
+
_
_
_
RL
vs
Rs
vL
+
-
iL
Power delivered to load is PL = i2L RL
Now
and
iL =
vs
RL + RS
i2L =
v2s
( RL + RS )2
…Contd !
Consider :
V2s RL
( RL + RS )2
PL =
V2s RL
( RL + RS )2

## Slide 3: Maximum Power …contd
If we want to determine the load at which the power will be maximum then we differentiate PL with respect to RLand equate it to zero.
So :
So maximum power transfer theorem states:-
“An independent voltage source in series with a resistance RS, or an independent current source in parallel with a resistance RS, delivers maximum power to that load resistance RL for which RL = RS.”
An alternate way is to state that “ A network delivers maximum power to a load resistance RL when RL is equal to the Thevenin’s equivalent resistance of the network.”
Contd !
dPL
( RL + RS )4
dRL
=
( RL + RS )2
V2s
_
V2s
( RL ) (2)
( RL + RS )
= 0
Then :
( RL + RS )2 =
( RL ) (2)
( RL + RS )
Or RL = RS
V2s RL
( RL + RS )2
PL =
V2s RL
( RL + RS )2

## Slide 4: Maximum Power …contd
In other words, maximum power is transferred to the load when the load resistance equals the Thevenin’s resistance as seen from the load (RL = RTh)
Consider :
Here, the power delivered to load is :
Contd !
+
_
_
_
RL
vTh
RTh
vL
+
-
iL
PL = i2L RL =
2
VTh
RTh + RL
RL
PL = i2L RL =
=
1
RTh + RL
2
RL
V2Th

## Slide 5: Maximum Power …contd
A plot shows :
Now for max power transfer :
Example !
PL
RL
RTh
Pmax
dPL
dRL
= 0
And RTh = RL
Also note that max power available from circuit :
Pmax =
V2Th
4 RTh
This is a quarter (not half half) of the power being generated.
PL =
1
RTh + RL
2
RL
V2Th

## Slide 6: Example : Maximum Power
Consider a 10 – volt source with RTh or internal resistance as 5 ohms. The maximum power it can generate is 20 watts.
The maximum power it can deliver to a load of 5 ohms is V2/R ie ¼ th of power being generated.
Best of Luck !
+
_
_
_
RL = 5Ω
vTh =10 v
RTh = 5 Ω
vL
+
-
iL

## Slide 7: The biggest risk in life is …not taking one. (Anonymous)