## Slide 2: Delta-Wye Conversion
Consider the following situation :
+
_
24 Ω
30 Ω
50 Ω
20 Ω
13 Ω
100V
a
b
10 Ω
Note that it is not possible to combine resistances by the rules of series and parallel addition.
Delta – Wye Conversion !

## Slide 3: Delta – Wye Conversion
Consider :
Rb
Ra
Rc
R1
R2
R3
Also called Δ to Y or π to T conversion.
It can be shown that :
And :
Ra =
R1
R1 R2 + R2 R3 + R1 R3
R1 =
Rb Rc
Ra + Rb + Rc
Rule!

## Slide 4
Notice :
Rb
Ra
Rc
R1
R2
R3
The conversion rules are:
  Each resistor in the Y network is the product of the resistors in the two adjacent Δ branches, divided by the sum of the three resistors.
  Each resistor in the Δ network is the sum of all possible products of Y resistors taken two at a time, divided by the opposite Y resistor.
Ra =
R1
R1 R2 + R2 R3 + R1 R3
R1 =
Rb Rc
Ra + Rb + Rc
Example !
Delta – Wye Conversion

## Slide 5: Circuit Analysis Techniques
We have learnt :
  KCL and
  KVL
    These two laws apply to any circuit because these enforce charge and energy conservation which are very fundamental principles.
  Based on KCL, we developed Nodal Analysis.
  Based on KVL, we developed Mesh Analysis (applicable only to planar circuits).
  Dealing with linear circuits allows us to use the principle of superposition.
  The technique of source transformation is another useful tool in circuit analysis.
  Finally Thevenin’s and Norton’s Theorem.
    And Maximum Power Transfer Theorem

## Slide 6: Communication skills are the most important skills any engineer can have. A very critical element in this tool set is the ability to ask a question and understand the answer, a very simple thing and yet it may make the difference between success and failure.
(James A Watson)