## Slide 2: Capacitors
Another building block of electrical/electronic circuits is the linear passive element called capacitor.
Resistors dissipate energy but capacitors (and inductors) store energy which can be retrieved at a later time. Hence these are called storage elements.
A capacitor consists of two conducting surfaces on which charge may be stored.
These surfaces are separated by a thin insulating layer, like air, paper or plastic etc, that has a very large resistance.
So ideally within the capacitor, R approaches infinity and hence charge cannot recombine.
Capacitors….contd!
| (
The leakage resistance is as high as 100 M ohms.
The passive sign convention is:
| (
i
C
+
-
v
The circuit symbol of a capacitor is :
For non – ideal capacitor :
| (

## Slide 3: Capacitors …contd
Capacitors ….contd!
The unit of capacitance is ampere – sec per volt.
Current ampere is coulomb per sec so capacitance is coulomb per volt (obvious from q=CV).
The capacitance of a capacitor is termed one farad (F) if it stores one coulomb of charge when the voltage across its terminals is one volt.
Or capacitance is the ratio of the charge on one plate of a capacitor to the voltage difference between the two plates.
Capacitors are designed to store electrical charge and capacitance is a measure of how much charge can a capacitor hold.
i = C
dv
dt
The voltage current relationship
Now it is obvious that :
q α V
q = C V
or
where C is the constant of proportionality.
Rearranging :
C = i
dt
dv
C =
dq
dv
dt
dt
X
or
When a voltage source is connected to a capacitor, it deposits a +ve charge ‘q’ on one plate and a -ve charge ‘- q’ on the other.

## Slide 4: Capacitors …contd
Capacitors …Contd!
The amount of charge that a capacitor can hold depends on the applied voltage. Therefore, like power rating of resistors, the capacitors are labeled with Working Voltage DC (WVDC) which should not be exceeded.
Recall :
R = ρ
L
A
Similarly :
where ε (epsilon) is permittivity
  This shows that ‘C’ is not dependent on ‘q’ or ‘v’ but on the physical dimensions of the capacitor.
Permittivity for air or vacuum is 8.854 pF/m.
Relative permittivity for vacuum is 1, and 1.0006 for air and 5.5 for mica and upto 7500 for ceramic.
Therefore permittivity is a measure of how easy it is to establish electric flux in a material.
It is different for various materials due to polarization of atoms in the insulating material called dielectric.
Permeability(μ)! ……Reluctance?
C = ε
A
d

## Slide 5: Capacitors …contd
Capacitors …contd !
A capacitor is charged when it is connected to a power source as shown :
  Plate of the capacitor that attaches to – ve terminal of the battery accepts electrons that the battery is producing.
  The plate of the capacitor that attaches to the + ve terminal of the battery loses electrons to the battery.
Capacitors and batteries both store electrical energy. Inside the battery, chemical reaction produces electrons on one terminal and absorbs electrons at the other terminal. A capacitor cannot produce electrons ; it only stores them.
One major difference between a capacitor and a battery is that a capacitor can dump its entire charge in a tiny fraction of a second.
-
+
+
-

## Slide 6: Capacitors …contd
Capacitors …contd !
Various applications of capacitors
  Flash gun
  To eliminate ripples
  Block dc voltages
  Capacitors, in association with inductors, create oscillators and so on.
A farad is a very large unit of capacitance. The capacitance of a capacitor is one farad if it stores one coulomb of charge when the voltage across its terminals is one volt.
A typical AA (1.5 volt) battery holds 2.8 ampere – hour.
That means it can produce 2.8 ampere for one hour at 1.5 volts (4.2 watt – hours).
Now one ampere – hour is 3600 amp – seconds.
Also one amp is one coulomb/sec. And a 1 – farad capacitor can store one coulomb of charge at one volt. Therefore 1 – farad capacitor can hold 1 amp at 1 volt.
Approximately 3600 X 2.8 = 10,080 farads to hold the energy of a typical AA battery (rounding off 1.5 to 1 volt).
Generally micro farad or pico farad are used.
Adjustable capacitors for fine adjustments are called trimmers.
| (
i
C
+
-
v

## Slide 7: Capacitors …contd
Capacitors …contd!
Charging of a capacitor.
Maxwell, a Scottish scientist, suggested that a “displacement current” flows between the plates. This is present whenever an electric field or voltage is varying with time. And displacement current is exactly equal to the conduction current.
Since the voltages and currents that exist during charging (and discharging) are transitory in nature, they are called transients.
Flow of current in a capacitor.
  Insulator between plates does not allow current (conduction).
t
vC
E
t
iC
(
+
_
t = 0
+
_
E

## Slide 8: Capacitors…contd
Note :
  Capacitors present open circuit to dc.
    Any AC signal flows through a capacitor because the capacitor will charge and discharge as the alternating current fluctuates making it appear that the AC is flowing.
  Constant voltage results in ‘0’ current ; because dv = 0
  Capacitor resists change in voltage abruptly because dt = 0 would mean infinite current.
Electrolytic capacitors :
  Provide large capacitance (several hundred thousand micro farad).
  Capacitance is large because they have a thin layer of oxide as their dielectric.
  Plate material is either aluminum or tantalum.
  During manufacture, chemical action creates a thin oxide layer that acts as the dielectric.
  This thin layer must be maintained during use hence electrolytic capacitors are marked + and - .
Capacitors …contd!

## Slide 9: Energy Storage (Electric Field) : Capacitors
We know :
dv
dt
C
i =
And : P = vi
or
dv
dt
C
P = v
or
dv
dt
v
P = C
Energy is :
dv
v
P dt = C
Integrating from 0 to t :
∫
t
t0
Pdt
=
C
∫
t
t0
vdv
If we select zero energy reference at to then :
wc(t) =
1
2
C
v2
joules
Capacitors …contd!

## Slide 10: Capacitors in Parallel
Consider the following arrangement :
Hence : Ceq= C1 + C2 + C3
Now : is = i1 + i2 + i3
(
+
_
(
+
_
(
+
_
v
is
+
_
i1
i1
i2
i1
i3
C1
C2
C3
And : Q1 = C1v Q2 = C2v Q3 = C3v and Qeq = Ceqv
So :
And :
i =
dQ
dt
(
+
_
v
is
+
_
Ceq
dQ3
dt
=
dQeq
dt
dQ2
dt
dQ1
dt
+
+
or
Q1 + Q2 + Q3 = Qeq
Therefore : C1v + C2v + C3v = Ceqv
Capacitors …contd!

## Slide 11: Capacitors in Series
Example !
Consider the following arrangement :
And two capacitors in series! Ceq = C1C2/(C1+C2)
Now : vs = v1 + v2 + v3
Because same charge appears on each plate hence :
Q = C1v1 Q = C2v2 Q = C3v3 and Q = Ceqvs
So :
And :
Q
C2
+
Q
C3
Q
C1
Q
Ceq
+
=
Therefore : 1/Ceq = 1/C1 + 1/C2 + 1/C3
(
+
_
i
Vs
+
_
Ceq
+
_
i
Vs
+
_
C1
v1
+
_
C2
v2
+
_
C3
v3
=
Q
Ceq
vs

## Slide 12: Capacitors Series & Parallel
Use 10 - μF capacitors rated at 300 V to design a capacitor bank of 40 – μF rated at 600 volts. Hint: Determine how many 10 - μF capacitors are needed and how would you connect these!
Solution:
  Four 10 - μF capacitors (each rated at 300 volts) in parallel will give us 40 - μF at 300 volts.
  So we can connect two 10 - μF capacitors in series to get 5 - μF at 600 volts.
  Eight of these 5 - μF at 600 volts (result of two 10 - μF capacitors in series) will provide us 40 – μF rated at 600 volts.

## Slide 13
Four things come not back:
the spoken word;
the sped arrow;
time past;
the neglected opportunity.
(Al Halif Omer Ibn)