## Slide 2: Inductors
In early 1800, Danish scientist Oersted demonstrated that a current –carrying conductor produced a magnetic field.
Ampere showed that magnetic field was linearly related to the current which produced it.
Faraday and Henry discovered that a changing magnetic field (due to di/dt) could induce a voltage in a neighbouring circuit. They showed that this voltage was proportional to the time rate of change of the current producing the magnetic field.
The constant of proportionality is what we now call the inductance symbolized by “L”;
The circuit symbol of an inductor :
Inductors …contd !
A non-ideal inductor can be modeled as shown.
  Notice the winding resistance. The winding capacitance is also called stray or parasitic capacitance.
    Coil is wound in sections to reduce capacitance.
An inductor is simply a coil of wire having magnetic properties.
| (

## Slide 3: Inductors…contd
Due to its discovery by American physicist Joseph Henry, the unit of inductance is henry (H) or volt – sec per ampere.
The inductance of a coil is one henry if a current changing at the rate of 1 ampere/sec creates a voltage of 1 volt.
Symbolically :
where A = cross sectional area
l or s = axial length of helix
N = number of turns
= permeability (relative permeability of air = 1 and steel has 2000)
Note that :
i
L
+
-
v
N2A
s or l
L
=
μ
μ
Inductors …contd !
{can be derived from Electromagnetic Theory}

## Slide 4: Inductors…contd
Inductance ‘L’ is defined by the voltage – current relationship :
Example Inductors!
i
L
+
-
v
v = L
di
dt
It shows that :
  Voltage across an inductor is proportional to rate of change of current through it.
  No voltage across an inductor carrying constant current.
  So inductor is a short circuit to dc.
  And most importantly, current in in an inductor cannot change instantaneously.
Features :
  When current starts flowing in the coil, the coil wants to build up a magnetic field.
  When the field is building up, the coil inhibits the flow of current.
  Once the field is built, current can flow normally through the coil.
  Inductors are also referred to as chokes, because they try to limit or choke current change.
Graphically :
t
iL
Slope is decreasing?
t
vL
t = 0

## Slide 5: Example : Inductors
If the waveform of the current in a 3 – H inductor is as shown, determine and sketch inductor voltage.
Example Inductors!
- 1
1
2
3
t (s)
i (t) A
1
Solution :
- 1
1
2
3
t (s)
v (t) V
3
- 3

## Slide 6: Capacitors/Inductors : Applications
Resistors and capacitors are commercially available as either discrete form or integrated-circuit (IC) form.
Unlike capacitors and resistors, inductors with appreciable inductance are difficult to produce on IC substrate.
Therefore inductors (coils) usually come in discrete form and tend to be more bulky and expensive; hence limited applications.
Inductors are used in relays, delays, sensing devices, telephone circuits, radio / TV etc.
Three important properties of capacitors and inductors are:-
  Temporary voltage or current sources. These can generate a large amount of current or voltage for a short period of time.
  Capacitors oppose abrupt changes in voltage and inductors oppose abrupt change in current.
  Capacitors and inductors are frequency sensitive. This property makes them useful for frequency discrimination.

## Slide 7: Think!