## Slide 1
Chapter 1
Overview of an Engineering Drawing

## Slide 2
TOPICS
Drawing standards
Projection methods
Orthographic projection
Graphics language
Engineering drawing

## Slide 3
TOPICS
Traditional Drawing Tools
Freehand Sketching
Lettering

## Slide 4: GRAPHICS LANGUAGE

## Slide 5
1. Try to write a description of
this object.
2. Test your written description
by having someone attempt to make a sketch from your
description.
Effectiveness of Graphics Language
The word languages are inadequate for describing the size, shape and features completely as well as concisely.
You can easily understand that …

## Slide 6
Graphic language in “engineering application” use
lines to represent the surfaces, edges and contours of objects.
A drawing can be done using freehand, instruments or computer methods.
Composition of Graphic Language
The language is known as “drawing” or “drafting” .

## Slide 7
Freehand drawing
The lines are sketched without using instruments other than pencils and erasers.
Example

## Slide 8
Instrument drawing
Instruments are used to draw straight lines, circles, and curves concisely and accurately. Thus, the drawings are usually made to scale.
Example

## Slide 9
Computer drawing
The drawings are usually made by commercial software such as AutoCAD, solid works etc.
Example

## Slide 10: Engineering Drawing

## Slide 11
Elements of Engineering Drawing
Engineering drawing are made up of graphics language
and word language.
Graphics
language
Describe a shape (mainly).
Word
language
Describe size, location and specification of the object.

## Slide 12
Basic Knowledge for Drafting
Graphics
language
Word
language
Line
types
Geometric
construction
Lettering
Projection
method

## Slide 13: PROJECTION METHOD

## Slide 14: PROJECTION METHOD
Perspective
Oblique
Orthographic
Axonometric
Multiview
Parallel

## Slide 15
PROJECTION THEORY
The projection theory is based on two variables:
1) Line of sight
2) Plane of projection (image plane or picture plane)
The projection theory is used to graphically represent
3-D objects on 2-D media (paper, computer screen).

## Slide 16
Line of sight is an imaginary ray of light between an
observer’s eye and an object.
Line of sight
Parallel projection
Line of sight
Perspective projection
There are 2 types of LOS :
parallel
converge
and

## Slide 17
Plane of projection is an imaginary flat plane which
the image is created.
The image is produced by connecting the points where
the LOS pierce the projection plane.
Parallel projection
Perspective projection
Plane of projection
Plane of projection

## Slide 18: Disadvantage of Perspective Projection
Perspective projection is not
used by engineer for manu-
facturing of parts, because
1) It is difficult to create.
2) It does not reveal exact
shape and size.
Width is distorted

## Slide 19: Orthographic Projection

## Slide 20: MEANING
5
Orthographic projection is a parallel projection technique
in which the parallel lines of sight are perpendicular to the
projection plane
Object views from top
Projection plane
1
2
3
4
5
1
2
3
4

## Slide 21: ORTHOGRAPHIC VIEW
Orthographic view depends on relative position of the object
to the line of sight.
Two dimensions of an
object is shown.
Three dimensions of an object is shown.
Rotate
Tilt
More than one view is needed
to represent the object.
Multiview drawing
Axonometric drawing

## Slide 22
Orthographic projection technique can produce either 1. Multiview drawing that each view show an object in two dimensions.
2. Axonometric drawing that show all three dimensions of an object in one view.
Both drawing types are used in technical drawing for communication.
NOTES
ORTHOGRAPHIC VIEW

## Slide 23
Axonometric (Isometric) Drawing
Easy to understand
Right angle becomes obtuse angle.
Circular hole becomes ellipse.
Distortions of shape and size in isometric drawing
Advantage
Disadvantage
Shape and angle distortion
Example

## Slide 24
Multiview Drawing
It represents accurate shape and size.
Advantage
Disadvantage
Require practice in writing and reading.
Multiviews drawing (2-view drawing)
Example

## Slide 25: Drawing Standard

## Slide 26: Introduction
Standards are set of rules that govern how technical drawings are represented.
Drawing standards are used so that drawings convey
the same meaning to everyone who reads them.

## Slide 27
ISO
International Standards Organization
Standard Code
ANSI
American National Standard Institute
USA
JIS
Japanese Industrial Standard
Japan
BS
British Standard
UK
AS
Australian Standard
Australia
Deutsches Institut für Normung
DIN
Germany
Country
Code
Full name
มอก.
สำนักงานมาตรฐานผลิตภัณฑ์อุตสาหกรรม
Thailand

## Slide 28
Partial List of Drawing Standards
มอก. 210 2520 วิธีเขียนแบบทั่วไป : ทางเครื่องกล
มอก. 440 ล.1 2541 การเขียนแบบก่อสร้างเล่ม 1 ทั่วไป
มอก. 446 ล.4 2532 ข้อแนะนำสำหรับการเขียนแผนภาพ วงจรไฟฟ้า
มอก. 1473 2540 การเขียนแบบเทคนิค การติดตั้ง สัญลักษณ์สำหรับระบบท่อของเหลว
ระบบทำความร้อน การระบายอากาศ
และระบบท่ออากาศ
Code number
Contents
ที่มา : http://library.tisi.go.th/data/lib_resources/pdf/catalog-online49/tis/02_ICS.pdf

## Slide 29
Partial List of Drawing Standards
JIS Z 8311 Sizes and Format of Drawings
JIS Z 8312 Line Conventions
JIS Z 8313 Lettering
JIS Z 8314 Scales
JIS Z 8315 Projection methods
JIS Z 8316 Presentation of Views and Sections
JIS Z 8317 Dimensioning
Code number
Contents

## Slide 30: Drawing Sheet
Trimmed paper of
a size A0 ~ A4.
Standard sheet size (JIS)
A4 210 x 297
A3 297 x 420
A2 420 x 594
A1 594 x 841
A0 841 x 1189
A4
A3
A2
A1
A0
(Dimensions in millimeters)

## Slide 31
Drawing space
Drawing
space
Title block
d
d
c
c
c
Border
lines
1. Type X (A0~A4)
2. Type Y (A4 only)
Orientation of drawing sheet
Title block
Sheet size(mm) c (mm) d (mm)
A4 10 25
A3 10 25
A2 10 25
A1 20 25
A0 20 25

## Slide 32
Drawing Scales
Scale is the ratio of the linear dimension of an element
of an object shown in the drawing to the real linear
dimension of the same element of the object.
Size in drawing
Actual size
Length, size
:

## Slide 33
Drawing Scales
Designation of a scale consists of the word “SCALE”
followed by the indication of its ratio, as follow
SCALE 1:1 for full size
SCALE X:1 for enlargement scales (X > 1)
SCALE 1:X for reduction scales (X > 1)
Dimension numbers shown in the drawing are correspond
to “true size” of the object and they are independent of
the scale used in creating that drawing.

## Slide 34
Basic Line Types
Types of Lines
Appearance
Name according
to application
Continuous thick line
Visible line
Continuous thin line
Dimension line
Extension line
Leader line
Dash thick line
Hidden line
Chain thin line
Center line
NOTE : We will learn other types of line in later chapters.

## Slide 35
Visible lines represent features that can be seen in the
current view
Meaning of Lines
Hidden lines represent features that can not be seen in the current view
Center line represents symmetry, path of motion, centers of circles, axis of axisymmetrical parts
Dimension and Extension lines indicate the sizes and location of features on a drawing

## Slide 36
Example : Line conventions in engineering drawing

## Slide 37: Traditional Drawing Tools

## Slide 38
DRAWING TOOLS

## Slide 39
1. T-Square
2. Triangles
DRAWING TOOLS

## Slide 40
3. Adhesive Tape
4. Pencils
2H or HB for thick line
4H for thin line
DRAWING TOOLS

## Slide 41
5. Sandpaper
6. Compass
DRAWING TOOLS

## Slide 42
7. Pencil Eraser
8. Erasing Shield
DRAWING TOOLS

## Slide 43
9. Circle Template
10. Tissue paper
DRAWING TOOLS

## Slide 44
11. Sharpener
12. Clean paper
DRAWING TOOLS

## Slide 45
ABCDEFGHIJKLMNOPQRSTUVWXYZABCDEFGHIJKLMNOPQRSTUVWXYZABCDEF
ABCDEFGHIJKLMNOPQRSTUVWXYZABCDEFGHIJKLMNOPQRSTUVWXYZABCDEF
Lettering

## Slide 46: Text on Drawings
Text on engineering drawing is used :
To communicate nongraphic information.
As a substitute for graphic information, in those instance where text can communicate the needed information more clearly and quickly.
Uniformity
- size - line thickness
Legibility
- shape
- space between letters and words
Thus, it must be written with

## Slide 47
Example
Placement of the text on drawing
Dimension & Notes
Notes
Title Block

## Slide 48: Lettering Standard
ANSI Standard
This course
Use a Gothic text style,
either inclined or vertical.
Use all capital letters.
Use 3 mm for most
text height.
Space between lines
of text is at least 1/3
of text height.
Use only a vertical Gothic
text style.
Use both capital and
lower-case letters.
Same. For letters in title block it is recommend to use 5~8 mm text height
N/A. Follows ANSI rule.

## Slide 49: Basic Strokes
Straight
Slanted
Curved
Horizontal
1
1
2
3
Examples : Application of basic stroke
“I” letter
“A” letter
1
2
3
4
5
6
“B” letter

## Slide 50
Suggested Strokes Sequence
Straight line
letters
Curved line
letters
Curved line
letters &
Numerals
Upper-case letters & Numerals

## Slide 51
The text’ s body height is about 2/3 the height of a capital letter.
Suggested Strokes Sequence
Lower-case letters

## Slide 52: Stroke Sequence
I
L
T
F
E
H

## Slide 53: Stroke Sequence
V
X
W

## Slide 54: Stroke Sequence
N
M
K
Z
Y
A
4

## Slide 55: Stroke Sequence
O
Q
C
G

## Slide 56: Stroke Sequence
D
U
P
B
R
J
1
2

## Slide 57: Stroke Sequence
5
7

## Slide 58: Stroke Sequence
6
8
9
0
S
3

## Slide 59
Stroke Sequence
l
i

## Slide 60
Stroke Sequence
v
w
x
k
z

## Slide 61
Stroke Sequence
j
y
f
r
t

## Slide 62
Stroke Sequence
c
o
a
b
d
p
q
e

## Slide 63
Stroke Sequence
g
n
m
h
u
s

## Slide 64
Word Composition
Look at the same word having different spacing between letters.
JIRAPONG
J
I
G
O
R
N
P
A
Which one is easier to read ?
A) Non-uniform spacing
B) Uniform spacing

## Slide 65
Word Composition
JIRAPONG
\ /
\
|
)(
)
|
(
|
Space between the letters depends on the contour of
the letters at an adjacent side.
Spacing
Contour
|
|
|
|
General conclusions are:
Good spacing creates approximately equal background area between letters.

## Slide 66
1. Straight - Straight
2. Straight - Curve
3. Straight - Slant
4. Curve - Curve
Space between Letters

## Slide 67
6. Slant - Slant
5. Curve - Slant
7. The letter “L” and “T”
≡
slant
slant
≡
slant
straight
Space between Letters

## Slide 68
GOOD
Not uniform in style.
Not uniform in height.
Not uniformly vertical or inclined.
Not uniform in thickness of stroke.
Area between letters not uniform.
Area between words not uniform.
Example : Good and Poor Lettering

## Slide 69
Leave the space between words equal to the space requires for writing a letter “O”.
Example
Sentence Composition
ALL
DIMENSIONS
ARE
IN
MILLIMETERS
O
O
O
O
UNLESS
OTHERWISE
SPECIFIED.
O

## Slide 73
Freehand Sketching

## Slide 74
Straight Line
1. Hold the pencil naturally.
2. Spot the beginning and end points.
3. Swing the pencil back and forth between the points, barely
touching the paper until the direction is clearly established.
4. Draw the line firmly with a free and easy wrist-and-arm motion

## Slide 75
Horizontal line
Vertical line

## Slide 76
Nearly vertical
inclined line
Nearly horizontal
inclined line

## Slide 77
Small Circle
Method 1 : Starting with a square
1. Lightly sketching the square and marking the mid-points.
2. Draw light diagonals and mark the estimated radius.
3. Draw the circle through the eight points.
Step 1
Step 2
Step 3

## Slide 78
Method 2 : Starting with center line
Step 1
Step 2
Step 3
1. Lightly draw a center line.
2. Add light radial lines and mark the estimated radius.
3. Sketch the full circle.
Small Circle

## Slide 79
Place the little finger (or pencil’ s tip) at the center as a pivot, and set the pencil point at the radius-distance from the center.
Hold the hand in this position and rotate the paper.
Large Circle

## Slide 80
Arc
Method 1 : Starting with a square
Method 2 : Starting with a center line

## Slide 81
Steps in Sketching
1. Block in main shape.
2. Locate the features.
3. Sketch arcs and circles.
4. Sketch lines.

## Slide 82
Example