## Slide 1: Lecture 2

## Slide 2: TYPES OF MEASURING SYSTEMS:
  English
      Feet and Inches
  Metric
      Meters and Millimeters

## Slide 3: Standard line types
- The various different looking lines used on technical or engineering drawings. Each style of line has a standard name, line thickness, pattern and meaning it conveys when used correctly. These lines are endorsed by both the ASME and ISO standards with minor variations.

## Slide 4: Object/visible line
Solid thick line Used to indicate visible object in a view.

## Slide 5: Hidden/Dashed line
Dashed Thin Line
Used to indicate hidden edges, corners hidden in a particular view

## Slide 6: Extension line
Thin Line
Used to extend the edge, face or corner of a geometric feature.

## Slide 7: Dimension line
Thin line with arrows
Used to indicate the size or location of the geometric feature

## Slide 8: Leader line
Thin line with arrow or dot
Used to indicate the size of geometric feature
Arrowheads touch object lines
Dots are placed on faces or surfaces

## Slide 9: Centerline/center point
Alternating long-short-long dashed thin line
Used to denote the axis of rotational parts or center point of holes

## Slide 10: Task-1

## Slide 11: Solution

## Slide 12: Symmetry lines
Centerline with 2 thick perpendicular track marks at each end
Used when partial symmetrical views are drawn

## Slide 13: Phantom line
Thin alternating long-short-short-long dashes
Used to indicate alternate positions of moving parts or repetitive features

## Slide 14: Cutting plane line
Thick phantom line with arrows or long dashed line with arrows
Used to indicate where an imaginary cut took place and direction it is viewed

## Slide 15: Section line/cross-hatching
Thin angled parallel lining
Used to indicate the faces cut by an imaginary cutting plane

## Slide 16: Break line
Thin lighting bolt line
Used to indicate the removal of a large portion of the part not needed in the view

## Slide 17
Choose line widths according to the size of the drawing from the following range: 0.13,0.18, 0.25, 0.35, 0.5, 0.7 and 1 mm.
BIS recommends two line widths on a drawing.
Ratio between the thin and thick lines on a drawing shall not be less than 1 : 2.

## Slide 18
When a Visible Line coincide with a Hidden Line or Center Line, draw the Visible Line. Also, extend the Center Line beyond the outlines of the view.
When a Hidden Line coincides with a Center Line, draw the Hidden Line.
When a Visible Line coincides with a Cutting Plane, draw the Visible Line.
When a Center line coincides with a Cutting Plane, draw the Center Line and show the Cutting Plane line outside the outlines of the view at the ends of the Center Line by thick dashes.

## Slide 19: Task-2

## Slide 20: Solution

## Slide 21: Task-3