## Slide 1: QUIZ ….only to Recap
How many terminals and regions are in BJT
How many junctions in BJT
BJT is asymmetric or symmetric device
How many types of BJT transistor are there
What are modes of operations of BJT
Why is emitter heavily doped while base is lightly doped
How does charges flow from emitter to collector
In which type of BJT current flows out of the base

## Slide 2: Affect of Base-emitter area on current

## Slide 3: Example
Determine the current Ix, if Q1 and Q2 are identical and operate in active mode and V1=V2

## Slide 4: Solution
Since
We have
The result can also be viewed as collector current of a single transistor having an emitter area of 2x A. In fact, redrawing the circuit and noting that Q1 and Q2, experiences identical voltages at their respective terminals, we say the two transistors are “parallel”, operating as a single transistor with twice the emitter area of each.

## Slide 5: Example:2
If we double Area of a transistor and decrease its Base-Emitter voltage by 60 mv . What is the change in collector current
Because of the double Area
=0.1 , decade decrease in current
So almost 5 times reduction in collector current

## Slide 7
Since
or

## Slide 8
Determine output voltage if
This current flows through RL , generating a voltage drop of 1.69 V

## Slide 9: Example: A transistor has a collector current of 1 mA and What is the value of VBE
Therefore VBE =778 mV
Now if β= 50,
This relationship you will understand in subsequent slides

## Slide 10: Current Flows
Basically Three types of currents
  Collector current
  Base Current
  Emitter Current

## Slide 11: DC Analysis of BJTs
Transistor Currents:
IE = IC + IB
alpha (DC)
IC = DCIE
beta (DC)
IC = DCIB
  DC typically has a value between 20 and 200

## Slide 12
NPN Transistor: Collector Current

## Slide 13: Important observations
Ic is independent of VCB
Is is inversely proportional to the base width W
Is is directly proportional to the area of the EBJ
Is typical values are between to A
Is is strong function of temp. doubles for every 5 Deg. Rise in Temp.

## Slide 14
NPN Transistor: Base Current
Note it is proportional to not equal to

## Slide 15
NPN Transistor: Base Current
β is in the range 50 to 200, but it can be as high as 1000 for special devices
The parameter β is called the common-emitter current gain

## Slide 16
NPN Transistor: Emitter Current
α is called the common-base current gain.

## Slide 17: Recapitulation
Basically, the forward-bias voltage VBE causes an exponentially related current iC to flow in the collector terminal.
The collector current Ic is independent of the value of the collector voltage as long as the collector–base junction remains reverse biased; that is, vCB ≥ 0.
Thus in the active mode the collector terminal behaves as an ideal constant-current source where the value of the current is determined by vBE. The base current iB is a factor 1/β of the collector current, and the emitter current is equal to the sum of the collector and base currents.
Since iB is much smaller than iC (i.e., β>> 1), iE = iC. More precisely, the collector current is a fraction α of the emitter current, with α smaller than, but close to, unity.

## Slide 18: Summary of the BJT current – voltage Relationship in Active Mode

## Slide 23: What is wrong here?
And desired
I wanted to have an output of 100mV ; it implies that I must have a resistance equal to

## Slide 24: How can I fix it
760mv
750mv
10 mv
1.7mA
2.48mA

## Slide 25: Biasing the transistor

## Slide 26: Lecture No 6 BJT

## Slide 27: DC Analysis
First question to be asked, In which mode is transistor operating?
A quick check of the terminal voltages will indicate whether the transistor is cut off or conducting
If conducting , we have to determine whether it is operating in the active mode or in saturation.
Using following step by step procedure we can determine the terminal voltages

## Slide 28: DC Analysis
Assume that the transistor is operating in Active mode
Check for consistency of the results with the FB conditions, the Vbe FB, Vcb RB more than -0.4 for NPN and lower than 0.4 for PNP; If yes the task is complete but if no then
Assume saturation mode:
Proceed to determine currents and voltages, then check for consistency of the result
Here important would be to calculate Ic/Ib ratio and verify that it is lower then the transistor beta

## Slide 29
We can see basically two loops BE and CE

## Slide 31: It is recommended to carry out the analysis directly on the circuit diagram. This way time can be reduce, if the steps are followed in proper sequence

## Slide 32: DC analysis BJT …….Cont..
Evaluate the voltages at all nodes and the currents through all branches in the circuit
By examining the circuit, we conclude that the two transistors Q1 and Q2 cannot be simultaneously conducting
But Why?
Now Assume Q2 is on then
current will flow from ground through the 1-kΩ resistor into the emitter of Q2. Thus the base of Q2 will be at a negative voltage, and
base current will be flowing out of the base through the 10-kΩ resistor and into the +5-V supply, which is not possible
In PNP the current flows out of Base

## Slide 33
0
0
The BE loop have two currents , The relationship is (between base and emitter with 1+β)

## Slide 34: Graphical Analysis of Exponential Model
Graphical analysis is performed by plotting the two Equations on the i–v plane. The solution can then be obtained as the coordinates of the point of intersection of the two graphs
Recall DIODE

## Slide 35: Applying same concept to Basic BJT Circuit
Input
Output

## Slide 36
Graphical Analysis: Locating Bias Point
Point Y : vBE = 0.5
Point Z : BJT leave the active mode
Determine Load Line
Which point on Load line
Set of Graphs
Note that we have set of graphs corresponding to each

## Slide 37
Bias point determined by the value of VBE and the load resistance RC
Two important considerations in deciding on the location of Q point:
  Gain
  Allowable signal swing at the output
  Gain can be increased by locating the Q point closer to point Z (saturation)
Graphical Analysis: Locating Bias Point
Z
More gain if small

## Slide 38
End point 1: saturation
End point 2: Cut off

## Slide 41
Note :As we increase IB The Q point moves upward, that is closer to saturation region

## Slide 42
With increasing R the slope decreases

## Slide 43
What is observation Here?

## Slide 44
III
II
I
BJT as a Switch

## Slide 47: Lets see what happens if we increase/decrease base voltage

## Slide 48
Why not in active mode??????

## Slide 49
0.96=0.64mA
We didn’t use
Value of ; when in saturation

## Slide 51
Here base at zero , does not mean in cutoff. Since it is a pnp transistor

## Slide 53
2
All these values indicates that not in active mode

## Slide 54
All currents are now with respect to. VB, using

## Slide 57: Short Break
LEC-6

## Slide 58: Sequence & Topics to be covered
Applying the BJT in Amplifier Design
Obtaining a Voltage Amplifier
The Voltage Transfer Characteristic (VTC)
Biasing the BJT to Obtain Linear Amplification
The Small-Signal Voltage Gain
Locating the Bias Point Q
Small-Signal Operation and Models
The Base Current and the Input Resistance at the Base
The Emitter Current and the Input Resistance at the Emitter
Voltage Gain
Separating the Signal and the DC Quantities
Application of the Small-Signal Equivalent Circuits
Augmenting the Small-Signal Models to Account for the Early Effect

## Slide 59: Further Example on DC Analysis
We try to find
Depending upon information available we start with either of the Loop
These will help us in calculating mode of operation and small signal parameters

## Slide 63
First Part is same as in 6.10, except
Old vc=8.6

## Slide 68: BJT as Amplifier

## Slide 69: BJT as Amplifier
when operated in the active mode, the BJT functions as a voltage-controlled current source: the base–emitter voltage controls the collector current
Although the control relationship is nonlinear (exponential), we will shortly devise a method for obtaining almost-linear amplification from this fundamentally nonlinear device.

## Slide 70
A voltage-controlled current source can serve as a transconductance amplifier, that is, an amplifier whose input signal is a voltage and whose output signal is a current
A simple way to convert a transconductance amplifier to a voltage amplifier is to pass the output current through a resistor and take the voltage across the resistor as the output.
BJT as Amplifier

## Slide 71: The Voltage Transfer Characteristic (VTC)
A very useful tool that yields great insight into the operation of an amplifier circuit is its voltage transfer characteristic (VTC). This is simply a plot of the output voltage versus the input voltage.( Graph)

## Slide 72
vO
Negative Slope

## Slide 73
Note that the output voltage is taken between the collector and ground, rather than simply across Rc. This is done because of the need to maintain a ground reference throughout the circuit. The output voltage is given by
The out put is 180 Deg. Phase shifted
(x-y) For Cutoff mode and
(y-Z) Active mode
Saturation mode
For greater than that at point Z,
the transistor operates in the saturation region and decreases very slowly

## Slide 74
The VTC indicates that the segment of greatest slope (and hence potentially the largest amplifier gain) is that labeled YZ, which corresponds to operation in the active mode. An expression for the segment YZ can be obtained by
This is obviously a nonlinear relationship.
linear (or almost-linear) amplification can be obtained by using the technique of biasing the BJT.

## Slide 75: Biasing the BJT to Obtain Linear Amplification
Biasing enables us to obtain almost-linear amplification from the BJT.
A dc voltage is selected to obtain operation at a point Q on the segment YZ of the VTC.
observe that the coordinates of Q are the dc voltages and which are related by

## Slide 76
Biasing BJT for Linear Amplification

## Slide 77
Biasing BJT for Linear Amplification

## Slide 78
Biasing BJT for Linear Amplification

## Slide 79
Next the signal to be amplified a function of time t is superimposed on the bias voltage . Thus the total instantaneous value of becomes

## Slide 80
The Small-Signal Voltage Gain

## Slide 81
The Small-Signal Voltage Gain

## Slide 82
We make the following observations on this expression for the voltage gain:
The gain is negative, which signifies that the amplifier is inverting; that is, there is a 180 phase shift between the input and the output
2. The gain is proportional to the collector bias current and to the load resistance

## Slide 83: Example 6.13
Consider an amplifier circuit using a BJT having IS = A, a collector resistance RC = 6.8 kΩ, and a power supply VCC = 10 V.
Determine the value of the bias voltage VBE required to operate the transistor at VCE = 3.2 V. What is the corresponding value of IC?
(b) Find the voltage gain Av at this bias point. If an input sine-wave signal of 5-mV peak amplitude is superimposed on VBE, find the amplitude of the output sine-wave signal (assume linear operation).
(c) Find the positive increment in vBE (above VBE) that drives the transistor to the edge of saturation,
where vCE = 0.3 V.
(d) Find the negative increment in vBE that drives the transistor to within 1% of cutoff (i.e., to vCE = 0.99VCC).

## Slide 85
Voltage gain X input Voltage= Output voltage

## Slide 87
Assignment # 4
Example :6.14 and
Problems: 6.28, 6.29, 6.39
Do not submit

## Slide 88: Small-Signal Operation and Models

## Slide 89
Small Signal Operation and Models

## Slide 90
Transconductance

## Slide 91
Transconductance
DC
SS
gm is the
“transconductance”

## Slide 92
Transconductance
gm varies with variation of Q point
The signal amplitude should be small enough that operation is restricted to an almost linear segment of the
iC-vBE exponential curve

## Slide 93
Base Current and Input Resistance

## Slide 94
Emitter Current and Input Resistance

## Slide 95
Also Do Exercise 6.36 and 6.37 as part of assignment
Did we use such eq. before?

## Slide 96
Voltage Gain

## Slide 97
Separating the DC & Signal Quantities
The total DC and Small signal circuit is shown.
The DC analysis yield the currents and voltages based on the relevant equations.
The DC sources do no change their values when the signal is applied.
We can replace DC voltages by short circuits and current sources by open circuits respectively to get the Small Signal Model.

## Slide 98
Separating the DC & Signal Quantities
The Small signal circuit is shown.
This circuit is useful only to analyze signal voltages and currents.
This is not an actual amplifier circuit.
This circuit shows all the incremental currents and voltages that occur due to applied small signal at the base.

## Slide 99: The Hybrid –π Model of BJT
Ie in terms of base resistance
Ie in terms of emitter resistance

## Slide 100
The T-Model of BJT

## Slide 101: Small-Signal Models Accounting for the Early Effect
The gain will be reduced, depending upon ro

## Slide 102
Example 6.14
Analyze the transistor amplifier shown in the Figure to determine its voltage gain vo/vi.
Assume β = 100.
Solution:
1. Determine the operating point. For this purpose.
assume vi = 0 and obtain the dc circuit.
The dc currents and voltage will be:
Since VB = 0.7 V is less than VC , the transistor is operating in the active mode

## Slide 103
2. Determine the small-signal model parameters:
3. Replace VBB and VCC with short circuits.
4. Replace the transistor in the circuit by hybrid-π, equivalent-circuit model
5. Analyze of the equivalent circuit

## Slide 104
5. Analyze of the equivalent circuit

## Slide 105: Steps for the Small-Signal Equivalent Circuits
Eliminate the signal source and determine the dc operating point of the BJT and in particular the dc collector current IC.
2. Calculate the values of the small-signal model parameters
3. Eliminate the dc sources by replacing each dc voltage source with a short circuit and each dc current source with an open circuit.
4. Replace the BJT with one of its small-signal equivalent circuit models.
5. Analyze the resulting circuit to determine the required quantities (e.g., voltage gain, input resistance.

## Slide 106
For DC analysis the signal source is removed

## Slide 108: Transconductance
Our study so far shows that the bipolar transistor acts as a voltage-dependent current source, when operating in the forward active region
But how we can quantify the performance of such a device, that is the measure of the goodness of a voltage dependent current source
Recalling the first lecture, the device becomes stronger as K increases, because as K is increased , results in larger output current thus larger output voltage
So we concentrate on the voltage –to-current conversion property of the transistor
If a signal changes the base-emitter voltage of a transistor by a small amount, how much change is produced in the collector current
The strength of the device can be represented by ∆Ic/ ∆Vbe
The ratio ∆Ic/ ∆Vbe approaches dIc/dVbe for very small changes in the limit, is called the “ Transconductance , gm

## Slide 109
The above equation reveals that as Ic increase, the transistor becomes a better amplifying device by producing larger collector excursions in response to a given signal level applied between the base and emitter
The transconductance may be expressed in or “siemens” S.
For example if Ic =1 mA, then with Vt =26 mv , we have

## Slide 110
If experiences a small perturbation ± ∆ V around then the collector current displays a change of × ∆ V around

## Slide 111
While considering the small signal notice the output is across Rc

## Slide 112: Performing small signal analysis directly on the circuit

## Slide 113: Small signal equivalent model with Early Effect

## Slide 114
Trans-conductance
VTC- Method
- Methd