## Slide 1
EE-260 : Electrical Machines
Lecture#11
INTRODUCTION (Page 230)
4.1 A SIMPLE LOOP IN A UNIFORM MAGNETIC FIELD (Page 230)
The Voltage Induced in a Simple Rotating Loop (Page 231)
4.4 INDUCED VOLTAGE IN AC MACHINES (Page 250)
Text Book: Chapter 04 (Stephen J. Chapman 4th Ed)
Instructor: Ms Neelma Naz
Class: BEE 12 C/D
School of Electrical Engineering and Computer Science
Department of Electrical Engineering

## Slide 2: Text Book: Chapter 04 (Stephen J. Chapman 4th Ed)
Fundamentals of Electrical Machines

## Slide 3: Introduction
Machine is a generic name both for the generator as well as motor.
A Machine can be:
a generator that converts
mechanical energy to electrical energy
or
a motor that converts
electrical energy to mechanical energy

## Slide 4: Introduction (cont...
Every Machine has two main parts with regards to its construction:
    Stator: The outer part of the machine, which is stationary, is called Stator.
    Rotor: The inner rotating part of the machine is called Rotor
3

## Slide 5
Any machine has two main windings:
  Field Winding: The one which produces main magnetic field in AC machines. Field winding is located on the rotor, therefore called field winding or rotor winding.
  Armature winding: Where the main voltage is induced. This winding is located on the stator, therefore called stator winding or Armature winding.
Introduction (cont...

## Slide 6
The two major classes of AC machines:
  Synchronous Machine: Magnetic field current is supplied by a DC power source. Mostly used as Generators (above 90% of the generators are Synchronous machines)
  Induction Machine: Field current is supplied by the magnetic induction (transformer action) into their field winding. Mostly used as motors (above 90% of the motors are induction machines)
Introduction (cont...

## Slide 7
AC Generator
(Field Fix Armature Rotating)
Will it work as AC Generator if the Armature is fixed and field is rotating ?
A Moving Loop in a Uniform Magnetic Field
7

## Slide 8
DC Machine:
Armature Rotating
Field Stationary
AC Machine: Armature Stationary Field Rotating
2-Poles Rotor

## Slide 9: Production of Induced Voltage on a Conductor Moving in a Magnetic Field
The Voltage induced in a wire moving in the magnetic field is:
“If the index finger points in the direction of flux, and the thumb indicates the movement of conductor, then the middle finger shows the direction of emf induced in the conductor”
Fleming’s Right Hand Rule:
The thumb, forefinger, and middle finger of the right hand are extended at right angles to each other.
Vector l points along the direction of the wire toward the end making the smallest angle with respect to the vector v×B

## Slide 10
A Moving Loop in a Uniform Magnetic Field
Z
S
a
b
c
d

## Slide 11
A simplest possible machine that produces ac voltage is a simple loop of wire rotating within a uniform magnetic field produced by a large stationary magnet
1.A Moving Loop in a Uniform Magnetic Field (cont…
The magnetic field is constant pointing from left to right and
the rectangular loop of the wire rotates
a voltage will be induced in the loop
The segment ab and cd are perpendicular to the plan of paper
&
segment bc and da are parallel to the plan of paper.

## Slide 12: 1.The Voltage Induced in a Rotating Loop
When the loop rotates in this magnetic field, voltage will be induced in it. The voltage on each segment is given by:
Into the page
Out of the page

## Slide 13
1.The Voltage Induced in a Rotating Loop (cont…

## Slide 14
The total induced voltage is the sum of the voltages induced on each side of the coil.
The resulting voltage eind is a function of angle as shown
1. The Voltage Induced in a Rotating Loop (cont..

## Slide 15
Substituting the two expressions in eq for eind.
The area of the loop is 2rl and the flux is the product of the loop’s surface area and flux density through the loop. Thus eind is:
Alternate way to express the equation, relating the behavior of single loop to the behavior of larger ac machines.
If the loop is rotating at a constant angular velocity ω, the angle theta of the loop will increase linearly with the time.
Also the tangential velocity v of the edges of the loop can be expressed as:
1. The Voltage Induced in a Rotating Loop (cont..

## Slide 16
The voltage induced in any real ac machine depends on three factors:
  The flux in the machine.
  The speed of rotation.
  A constant representing the construction of the machine
  ( the number of loop etc.)
The maximum flux occurs when the loop is perpendicular to the magnetic flux density lines.
The voltage generated in the loop is a sinusoid whose magnitude is equal to the product of the flux inside the machine and the speed of rotation of the machine.
1. The Voltage Induced in a Rotating Loop (cont..

## Slide 17: 2. Induced Voltage in AC Machines
Fig. shows a rotating magnetic field on the rotor and a stationary coil in the stator.
4.4 p250

## Slide 18: 2. Induced Voltage in AC Machines (cont…
The equation, for the voltage induced, was derived for the case of a moving wire in a stationary magnetic field, while now the wire is stationary and the magnetic field is moving.
To use it we must be in the frame of reference where the magnetic field is stationary and the wire is moving. The sides of the stator coil will appear to go by at an apparent velocity Vrel and the equation can be applied.
Thus the voltage induced in a single turn coil is:
Finally, if the stator coil has N turn then the total voltage induced in the coil is:

## Slide 19: 3. Induced Voltage in a Three Phase Set of Coils
If three coils, each of Nc turns, are placed at intervals of 120o around the rotor magnetic field, the voltage induced in each of them will be the same in magnitude but differ in phase by 120o.
Thus a rotating magnetic field will generate a three-phase set of voltages in a stator.

## Slide 20: The RMS Voltage in a Three Phase Stator
The rms terminal voltage of the machine will depend on whether the stator is Y or ∆ connected.
The peak voltage in any phase can be expressed as:
The rms voltage of any phase of the three phase stator is:
For Y connected machine
For ∆ connected machine

## Slide 21: Generator Action
Example 4-2:
The following information is known about the simple two-pole generator in the Figure. The peak flux of the rotor magnetic field is 0.2 T, and the mechanical rate of rotation of the shaft is 3600 r/min. The stator diameter of the machine is 0.5 m, its coil length is 0.3 m, and there are 15 turns per coil. The machine is Y-connected.
  What are the three phase voltages of the generator as a function of time?
  What is the rms voltage of this generator?
  What is the rms terminal voltage of this generator?

## Slide 22
The flux is given by:
Solution
The rotor speed is:
(a) Magnitudes of the peak phase voltages
The three phase voltages
(b) The rms phase voltage
(c) The terminal rms voltage
9

## Slide 24: 4. The Motor Action
4.1: A Current-Carrying Loop in a Uniform Magnetic Field
  The torque induced in a current-carrying loop
4.5: Induced Torque in an AC Machine

## Slide 25: Production of Induced Force on a Current Carrying Wire
The force induced on the conductor is:
“If the index finger of right hand points in the direction of the vector l and the middle finger points in the direction of flux density vector B, then the thumb points in the direction of the resultant force F on the wire.”
The thumb, forefinger, and middle finger of the right hand are extended at right angles to each other.
Fleming’s Right Hand Rule:
Direction of l defined to be in the direction of current flow
REVIEW

## Slide 26: 4. The Torque Induced in a Current-Carrying Loop (1/8)
To determine the magnitude and direction of torque, first the force on each segment of the loop is calculated:
Assume that the rotor loop is at some arbitrary angle θ with respect to the magnetic field, and current is flowing in the loop
Torque will be induced on the wire loop

## Slide 27: 4. The Torque Induced in a Current-Carrying Loop (2/8)

## Slide 28: 4. The Torque Induced in a Current-Carrying Loop (3/8)
Segment ab: The direction of current is into the page, while the magnetic field B points to the right, the vector lxB points down. The induced force and torque are:
Segment bc: The direction of current is in the plan of the page, while the magnetic field B points to the right. The vector lxB points into the page. The the induced force and torque are:

## Slide 29: 4. The Torque Induced in a Current-Carrying Loop (4/8)
Segment cd: The direction of current is out of the page, while the magnetic field B points to the right, the vector lxB points up. The induced force and torque are:
Segment da: The direction of current is in the plan of the page, while the magnetic field B points to the right. The quantity lxB points out the page. Thus the induced force and torque are:

## Slide 30: 4. The Torque Induced in a Current-Carrying Loop (5/8)
The resulting torque is shown as a function of angle
The torque is maximum when the plane of the loop is parallel to the magnetic field
The torque is zero when the plane of the loop is perpendicular to the magnetic field
The total induced torque on the loop is the sum of the torques on each of its side.

## Slide 31: 4. The Torque Induced in a Current-Carrying Loop (6/8)

## Slide 32: 4. The Torque Induced in a Current-Carrying Loop (7/8)
G depends upon the geometry of the loop
The equation can be alternatively expressed in terms of the flux density produced due to current in the loop
If the current in the loop is as shown in the figure , it will produce magnetic flux density Bloop.
The magnitude of the flux density will be:
Loop area is equal to 2rl

## Slide 33: 4. The Torque Induced in a Current-Carrying Loop (8/8)
The torque induced in the loop and also in general the torque in any real ac machine depends on four factors:
  The strength of the rotor magnetic field
  The strength of the external magnetic field
  The angle between the two magnetic fields
  A constant representing the construction of the machine (geometry).
k depends upon construction of the machine, Bs is the stator magnetic field
The torque eq. can be expressed as a cross product

## Slide 34
Conclusion
Introduction
Moving loop in uniform magnetic field
Voltages induced in rotating loop
Induced voltages in AC machines
Induced voltages in three phase set of coils