## Slide 1: Chapter No8_1

## Slide 2: What we studied so far
Philosophy of integrated circuits
Basic gain cells
Cascoding
Currents sources and mirrors
Improving basic current sources
Other transistor combinations

## Slide 3: Differential Amplifier
Chapter No 8

## Slide 4: Differential Inputs generation

## Slide 5: Why Differential?
One of the most widely used analog block
  High-performance mixed-signal circuits
Differential circuits are much less sensitive to noise and interference than single-ended circuits.
Differential configuration enables us to bias the amplifier and to couple amplifier stages together without the need for bypass and coupling capacitors
A mixed-signal integrated circuit is any integrated circuit that has both analog circuits and digital circuits on a single semiconductor die. ... Mixed-signal circuits or systems are typically cost-effective solutions for building any modern consumer electronics, industrial, medical, measurement, space etc.

## Slide 6: Interference and noise in signals
In telecommunications, an interference is that which modifies a signal in a disruptive manner, as it travels along a communication channel between its source and receiver. The term is often used to refer to the addition of unwanted signals to a useful signal. Common examples include:
Electromagnetic interference (EMI)
Co-channel interference (CCI), also known as crosstalk
Adjacent-channel interference (ACI)
Intersymbol interference (ISI)
Inter-carrier interference (ICI), caused by doppler shift in OFDM modulation (multitone modulation).
Common-mode interference (CMI)
Conducted interference
Noise is a form of interference but not all interference is noise.

## Slide 7: Thermal Noise
Thermal noise is generated naturally by thermal agitation of electrons in a conductor commonly found in opto-electronic devices. ... In communication, thermal noise has a major influence to the quality of the receiver. The lower the thermal noise the higher and more expensive is receiver sensitivity.

## Slide 9: Example
Diff circuit more immune to noise
e.g. Power Supply Noise
  Single-Ended:
    Supply varies by DV  Vout changes by approx. same amount
  Differential (symmetric circuit)
    Noise on supply affects VX and VY, not VX-VY (Vout)
    High-Noise Immunity – rejects common signal (noise)

## Slide 10: Another advantage of diff amp.
In a single CS amplifier, the maximum swing is VDD-(VGS-VTH)
In a differential pair it can be shown that the swing of VX-VY can reach 2[VDD-(VGS-VTH)].

## Slide 11: Differential Amplifier: Config. & modes
Configurations
Modes of Operation
  Common mode
  Differential mode
Dual input balanced output differential amplifier.
Dual input, unbalanced output differential amplifier.
Single input, balanced output differential amplifier.
Single input, unbalanced output differential amplifier.

## Slide 12: Configurations

## Slide 13: Configurations

## Slide 14: DIFFERENTIAL AMPLIFIER definitions
Common mode rejection ratio (CMRR)
  CMRR is a measure of how well the differential amplifier rejects the common-mode input voltage in favor of the differential-input voltage.
Input common-mode range (ICMR)
  The input common-mode range is the range of common-mode voltages over which the differential amplifier continues to sense and amplify the difference signal with the same gain.
  Typically, the ICMR is defined by the common-mode voltage range over which all MOSFETs remain in the saturation region.
Output offset voltage (VOS(out))
  The output offset voltage is the voltage which appears at the output of the differential amplifier when the input terminals are connected together.
Input offset voltage (VOS(in) = VOS)
  The input offset voltage is equal to the output offset voltage divided by the differential voltage gain.

## Slide 15: Circuit diagrams of basic differential Pairs
Basic MOS differential Pair
Basic BJT differential Pair

## Slide 16: Differential Transistor Pairs
MOSFET Diff-Pair
BJT Diff-Pair
The bottom transistor (the one with Ibias) sets the total current
The upper two transistors compete for a fraction of this current

## Slide 17: COMMON MODE OPERATION

## Slide 18
Since and are matched, the current I will divide equally
between the two transistors. Thus,
and the voltage at the sources, , will be
where is the gate-to-source voltage corresponding to a drain current of . Neglecting channel-length modulation, and are related by
Or in terms of the overdrive voltage

## Slide 19
= 0

## Slide 20: Input common-mode range