## Slide 1: Chapter4: Combinational Logic
Lecture3- Design 4-bit Lookahead Carry Binary Adder-Subtractor Circuit
Engr. Arshad Nazir, Asst Prof
Dept of Electrical Engineering
SEECS

## Slide 2: Objectives
Explore the problems associated with Ripple Carry Adder Design
Redesign an alternate 4-Bit Binary Adder-Subtractor Circuit i.e. Look ahead Carry Binary Adder to overcome long propagation delays encountered in the previous adder design
Study overflow in arithmetic circuits

## Slide 3: 4-Bit Binary Adder
A binary adder is a digital circuit that produces the arithmetic sum of two binary numbers.
A binary adder can be implemented using multiple full adders (FA) connected in cascade with the output carry from each full adder to the input carry of the next full adder in the chain

## Slide 4: Carry Propagation
The addition of two binary numbers in parallel implies that all the bits of the augend and addend are available for computation at the same time
In any combinational circuit, the signal must propagate through the gates before the correct output is available in the output terminals.
The Total propagation time = propagation delay of a typical gate X the number of gate levels
The longest propagation delay time in a binary adder is the time it takes the carry to propagate through the full adders.
This is because each bit of the sum output depends on the value of the input carry. This makes the binary adder very slow.

## Slide 5: Carry Propagation
Since each bit of the sum output depends on the value of input carry, the value of Si in any given stage in the adder will be in its steady state final value only after the input carry to the stage has been propagated
Consider output S3 in Figure 4-9. Inputs A3 and B3 are available as soon as input signals are applied to the adder, however input carry C3 doesn’t settle to its final value until C2 is available from the previous stage
Similarly C2 has to wait for C1 and so on down to C0
In this way only after the carry propagates and ripples through all stages will the last output S3 and carry C4 settle to their final correct value

## Slide 6: Carry Propagation
The number of gate levels for the carry propagation can be found from the circuit of the full adder
The input and output variables use the subscript i to denote a typical stage in the adder
The signals at Pi and Gi settle to their steady state values after they propagate through their respective gates

## Slide 7: Carry Propagation
These two signals are common to all full adders and depend only on the augend and addend bits
The signal from the input carry Ci to the output carry Ci+1 propagates through an AND gate and an OR gate, which constitutes two gate levels
If there are four full adders in the adder, the output carry C4 would have 2 x 4 = 8 gate levels from C0 to C4.
For an n-bit adder, there are 2n gate levels for the carry to propagate from input to output
The outputs of a combinational circuit will not be correct unless the signals are given enough time to propagate through the gates connected from inputs to outputs
All other arithmetic operations are implemented by successive additions, the time consumed during the addition process is very critical.

## Slide 8: Carry Propagation
One choice to reduce the carry propagation delay is to employ faster gates but the most widely used technique for reducing the carry propagation time in parallel adder is principle of carry lookahead
Consider the circuit of full adder shown in fig 4-10
If we define two binary variables
  carry propagate: Pi = AiBi (Term associated with the propagation of carry from Ci to Ci+1)
  carry generate: Gi = AiBi (Produces 1 when both Ai and Bi are 1)
Output sum and carry can be expressed as
  sum: Si = PiCi
  Carry: Ci+1 = Gi+PiCi

## Slide 9: Carry Propagation
We now write the Boolean functions for the carry outputs of each stage and substitute for each Ci, its value from the previous equation
  Co= input carry
  C1 = G0+P0C0
  C2 = G1+P1C1
  = G1+P1(G0+P0C0)
  = G1+P1G0+P1P0C0
  C3 = G2+P2C2
  = G2+P2G1+P2P1G0+ P2P1P0C0
  C4 = G3+P3C3
  =G3+P3G2+P3P2G1+P3P2P1G0+P3P2P1P0C0
Since the Boolean function for each output carry is expressed in sum of products, each function can be implemented with one level of AND gates followed by an OR gate (or by two-level NAND)

## Slide 10: Carry Look ahead Generator
The four Boolean functions for C1, C2, C3 ,and C4 are implemented in the carry look ahead generator shown in Figure 4-11
Here C4 doesn’t have to wait for C3, C2 and C1 to propagate and C4 is propagated at the same time as C1, C2, and C3.

## Slide 11: Carry Look ahead Generator
Fig 4-11 Logic Diagram of Carry Look ahead Generator

## Slide 12: 4-Bit Adder with Carry Look ahead
The construction of 4-bit adder with a carry lookahead generator is shown in Figure 4-12
Each sum output requires two exclusive-OR gates.
The output of first exclusive-OR gate generates the Pi variable and the AND gate generates the Gi variable
The carries are propagated through the carry look ahead generator and applied as inputs to the second exclusive-OR gate
All outputs carries are generated after a delay through two levels of gates
Outputs S1 through S3 have equal propagation delay times

## Slide 13: 4-Bit Adder with Carry Look ahead

## Slide 14: Binary Subtractor
The subtraction of unsigned binary numbers can be easily done by means of complements.(section 1-5)
A-B = A+(2’s complement of B)
The 2’s complement can be obtained by taking the 1’s complement and adding 1 to least significant pair of bits
To obtain 2’s complement, the 1’s complement can be implemented with inverters and one can be added to the sum through the input carry

## Slide 15: Binary Subtractor
The circuit for subtracting A – B consists of an adder with inverters placed between each data input B and the corresponding input of full adder
The input carry C0 must be equal to 1 when performing subtraction
The operation thus performed becomes A plus the 1’s complement of B plus 1 (A+1’s complement of B+1). This is equal to A plus 2’s complement of B (A+2’s complement of B)
For unsigned numbers this gives A – B if A ≥ B or the 2’s complement of (B – A) if A<B

## Slide 16: Binary Subtractor
The addition and subtraction operation can be combined into one circuit with one common binary adder
This is done by including an exclusive-OR gate with each full adder
The mode input M controls the operation. When M=0, we have B0= B. The full adder receives the value of B, the input carry is 0 and the circuit performs A+B
When M=1, we have B1= B’. The full adder receives the value of B’, the input carry C0 is 1 and the circuit performs A plus the 2’s complement of B. (A+1’s complement of B+1).
The exclusive-OR with output V is for detecting an overflow (detail later, in overflow)

## Slide 18: Overflow
When two numbers of n digits are added and sum occupies n+1 digits we say that an overflow occurred
Overflow is problem in digital computers because the number of bits that hold the number (limited storage) is finite and a result that contains n+1 can’t be accommodated.
The detection of an overflow after the addition of two binary numbers depends on whether the numbers are considered to be signed or unsigned
When two unsigned numbers are added an overflow is detected from the end carry out of the most significant position
In the case of signed numbers, the leftmost bit always represent the sign and negative numbers are in 2’s complement form

## Slide 19: Overflow
When two signed numbers are added, the sign bit is treated as part of the number and end carry doesn’t indicate an overflow
An overflow can’t occur after an addition if one number is positive and the other is negative, since adding a positive number to a negative number produces a result which is smaller than the larger of the two original numbers.
An overflow may occur if the two numbers added are both positive or both negative
For n-bit registers, the range of numbers (signed numbers) that each register can accommodate is from binary 2n-1-1 to binary –2n-1.

## Slide 20: Overflow
For 8-bit registers, the range of numbers that each register can accommodate is from binary +127 to binary –128
Consider two signed numbers +70 and +80 stored in two 8-bit registers. The sum of two numbers is +150 which exceeds the capacity of eight bit register
Note: Negative numbers are in 2’s complement form

## Slide 21: Overflow
If we just consider the 8-bit result from the last example, we go wrong as we
  Add two positive numbers and obtain a negative number
  Add two negative numbers and obtain a positive number
The carry out of sign bit position is taken as the sign bit of the result, then the 9-bit answer so obtained will be correct. This answer can’t be accommodated within 8-bits we say that an overflow has occurred
An overflow has occurred if carry into the sign bit position and carry out of the sign bit position are not equal. This can be found by applying the two carries to an exclusive-OR gate. 1 at the output of the gate indicates overflow
  V=0, no overflow; V=1, overflow

## Slide 22: The End